ICE
Workbook

09/12/19
Draft Version 1.0

Copyright International Business Machines Corporation 2019 IBM, the IBM logo, and ibm.com are trademarks or registered trademarks of International Business Machines Corp., registered in many jurisdictions worldwide. Other product and service names might be trademarks of IBM or other companies. A current list of IBM trademarks is available on the Web at “Copyright and trademark information” at www.ibm.com/legal/copytrade.shtml. The OpenCAPI word mark and the OpenCAPI Logo mark, and related marks, are trademarks and service marks licensed by the OpenCAPI Consortium.

# Overview
The ICE core includes the OpenCAPI 3.1 TLx reference design, as well as components such as the AFU main data flow logic, Asynchronous crossing domain and Memory controller user interface. On the ICE top, Xilinx GTY transceiver communicates to host through x8 OpenCapi Lanes and Xilinx DDR4 Memory Interface IPs connected to the 32GB of DDR4 memory. The entire ICE RTL will be built on Xilinx Zynq UltraScale+ FPGA ZU19EG-2FFVC1760I.
The Xilinx GTY transceiver can be generated to support line rate of either 21.33Gb/s or 25.6Gb/s. The transceiver is running 64:1 clock ratio between the OpenCAPI and ICE AFU main logic which operates at 333Mhz/400Mhz.
The Xilinx DDR4 memory interface IP is generated to support max data rate of 2133 Mb/s DDR speed. The max rate of 2133 Mb/s is due to the limitation of Xilinx memory interface IP of supporting the DDP memory devices used by ICE. The memory interface IP has 1066Mhz frequency is running 4:1 clock ratio to user interface logic which operates at 266Mhz. There are asynchronous buffers in-between 333Mhz/400Mhz domain and 266Mhz domains. Two DDR4 memory ports design each has max bandwidth of 19GB/s.
## Chip Overview
ICE only supports 64B or 128B wr_mem and rd_mem. pr_rd_mem and pr_wr_mem are also supported for ICE MMIO access. ICE doesn't support 256B, 32B, PADMEM operations and ICE returns credit (VC3) for mem_cntl ops. Only subset of OpenCAPI templates are supported by ICE. ICE OpenCAPI 3.1 RX supports template x”00”, x”01” and x”04. ICE OpenCAPI 3.1 TX supports template x”00”, x”01” and x”05”. ICE doesn’t support template x’07’, x’09’, x’A’ and 0x’B’. ICE doesn’t support OpenCAPI Lane width degrade.
## Design Details

- 2 memory ports design.
- 16GB and 2 ranks per port with total of 32GB.
- 9 devices per port with total of 18 devices.
- Using Micro Twin Die (MT40A2G8) x8.
- 72b wide per port.
- Address translation for DDR4 is fixed. Port bit is defined at 128B offset
- Early write done response.
  - Note: Xilinx memory controller in ICE doesn't allow same address to pass in the event that if host ceases address protection upon receive early write done.
- Data + meta data + Parity
- PHY - 21.33GHz/25.6GHz. Xilinx IP
- DLX/TLX - 333Mhz/400Mhz. Modify opencapi 3.0 reference design to support openCapi 3.1 and meta data
- AFU - Consist two frequency domains responsible for communication with TLX reference design and Xilinx Memory controller
- 400Mhz domain handles communication with TLX reference design
- 266Mhz domain handles communication with Xilinx Memory controller IP
- MC - 1066Mhz Xilinx memory controller IP.
- DDR4 - 2133Mhz

## High Level Mainline Data Flow

## Design Organization
- ice_top
  - ice_core
    - ice_afu_mac
      - ice_tlx_top
        - ice_tlx_rcv
        - ice_tlx_framer
      - ice_afu_cfg
      - ice_errrpt_intrp
      - ice_mmio_mac
      - ice_mem_init
      - ice_afu_main
      - ice_afu_ui
        - ice_gmc_top
    - ice_cal_retry
    - ice_mc_top
      - ddr4_p0
      - ddr4_p1
  - dlx_phy_wrap
  - ice_pervasive
## ICE Core I/O
Signal Name	I/O	Size	Description	Clock Domain
DDR4 PORT0 PHY INTERFACE
c0_sys_clk_p	IN	1	Input reference clock for Xilinx MIG
c0_sys_clk_n	IN	1	Input reference clock for Xilinx MIG
c0_ddr4_cke	OUT	2	Clock Enable
c0_ddr4_ck_c	OUT	1	DRAM Clock. ck_c and ck_t are differential clock
c0_ddr4_ck_t	OUT	1	DRAM Clock. ck_c and ck_t are differential clock
c0_ddr4_cs_n	OUT	2	Chip Select
c0_ddr4_odt	OUT	2	On Die Termination
c0_ddr4_act_n	OUT	1	Activation Command begin entered along with CS_n
c0_ddr4_adr	OUT	17	Provide the row address for ACTIVATE Commands and the column address for Read/Write commands to select one location out of the memory array in the respective bank. (A10/AP, A12/BC_n, RAS_n/A16, CAS_n/A15 and WE_n/A14 have additional functions)
c0_ddr4_dm_dbi_n	INOUT	9	Input Data Mask and Data Bus Inversion
c0_ddr4_bg	OUT	2	Bank Group
c0_ddr4_ba	OUT	2	Bank Address
c0_ddr4_dq	INOUT	72	Data input/output
c0_ddr4_dqs_c	INOUT	9	Data Strobe
c0_ddr4_dqs_t	INOUT	9	Data Strobe
c0_ddr4_reset_n	OUT	1	Active low Asynchronous Reset
DDR4 PORT1 PHY INTERFACE
c1_sys_clk_p	IN	1	Input reference clock for Xilinx MIG
c1_sys_clk_n	IN	1	Input reference clock for Xilinx MIG
c1_ddr4_cke	OUT	2	Clock Enable
c1_ddr4_ck_c	OUT	1	DRAM Clock. ck_c and ck_t are differential clock
c1_ddr4_ck_t	OUT	1	DRAM Clock. ck_c and ck_t are differential clock
c1_ddr4_cs_n	OUT	2	Chip Select
c1_ddr4_odt	OUT	2	On Die Termination
c1_ddr4_act_n	OUT	1	Activation Command begin entered along with CS_n
c1_ddr4_adr	OUT	17	Provide the row address for ACTIVATE Commands and the column address for Read/Write commands to select one location out of the memory array in the respective bank. (A10/AP, A12/BC_n, RAS_n/A16, CAS_n/A15 and WE_n/A14 have additional functions)
c1_ddr4_dm_dbi_n	INOUT	9	Input Data Mask and Data Bus Inversion
c1_ddr4_bg	OUT	2	Bank Group
c1_ddr4_ba	OUT	2	Bank Address
c1_ddr4_dq	INOUT	72	Data input/output
c1_ddr4_dqs_c	INOUT	9	Data Strobe
c1_ddr4_dqs_t	INOUT	9	Data Strobe
c1_ddr4_reset_n	OUT	1	Active low Asynchronous Reset
OpenCAPI Channels
CAPI_FPGA_LANE_N	IN	8	OpenCAPI RX Lane
CAPI_FPGA_LANE_P	IN	8	OpenCAPI RX Lane
FPGA_CAPI_LANE_N	OUT	8	OpenCAPI TX Lane
FPGA_CAPI_LANE_P	OUT	8	OpenCAPI TX Lane
CAPI_FPGA_REFCLK_N	IN	2	Transceiver reference clock
CAPI_FPGA_REFCLK_P	IN	2	Transceiver reference clock
Clock & Reset
freerun_CLOCK_N			Global reference clock
freerun_CLOCK_P			Global reference clock
RESETN	IN	1	Asynchronous reset

## FPGA I/O pin assignment
PIN AB35 => CAPI_FPGA_REFCLK_N[0] / PIN AB34 => CAPI_FPGA_REFCLK_P[0] / PIN W41 => CAPI_FPGA_LANE_P[0] / PIN W42 => CAPI_FPGA_LANE_N[0] / PIN Y34 => FPGA_CAPI_LANE_P[0] / PIN Y35 => FPGA_CAPI_LANE_N[0] / PIN V39 => CAPI_FPGA_LANE_P[1] / PIN V40 => CAPI_FPGA_LANE_N[1] / PIN W36 => FPGA_CAPI_LANE_P[1] / PIN W37 => FPGA_CAPI_LANE_N[1] / PIN U41 => CAPI_FPGA_LANE_P[2] / PIN U42 => CAPI_FPGA_LANE_N[2] / PIN V34 => FPGA_CAPI_LANE_P[2] / PIN V35 => FPGA_CAPI_LANE_N[2] / PIN T39 => CAPI_FPGA_LANE_P[3] / PIN T40 => CAPI_FPGA_LANE_N[3] / PIN U36 => FPGA_CAPI_LANE_P[3] / PIN U37 => FPGA_CAPI_LANE_N[3] / PIN A7 => SDA_IO / PIN B7 => SCL_IO / PIN D9 => RESETN / PIN G18 => c0_ddr4_dqs_t[8] / PIN F18 => c0_ddr4_dqs_c[8] / PIN G30 => c0_ddr4_dqs_t[0] / PIN F30 => c0_ddr4_dqs_c[0] / PIN B17 => c0_ddr4_dqs_t[4] / PIN A17 => c0_ddr4_dqs_c[4] / PIN B13 => c0_ddr4_dqs_t[3] / PIN A12 => c0_ddr4_dqs_c[3] / PIN B25 => c0_ddr4_dqs_t[7] / PIN B26 => c0_ddr4_dqs_c[7] / PIN H23 => c0_ddr4_dqs_t[6] / PIN G23 => c0_ddr4_dqs_c[6] / PIN E26 => c0_ddr4_dqs_t[2] / PIN E27 => c0_ddr4_dqs_c[2] / PIN D34 => c0_ddr4_ck_t[0] / PIN C34 => c0_ddr4_ck_c[0] / PIN M15 => c0_ddr4_dqs_t[5] / PIN L15 => c0_ddr4_dqs_c[5] / PIN L24 => c0_ddr4_dqs_t[1] / PIN K24 => c0_ddr4_dqs_c[1] / PIN C30 => c0_ddr4_act_n / PIN B32 => c0_ddr4_adr[1] / PIN A29 => c0_ddr4_adr[10] / PIN B31 => c0_ddr4_adr[12] / PIN B30 => c0_ddr4_adr[14] / PIN E32 => c0_ddr4_adr[15] / PIN C31 => c0_ddr4_adr[16] / PIN C36 => c0_ddr4_adr[4] / PIN A35 => c0_ddr4_adr[6] / PIN A32 => c0_ddr4_adr[3] / PIN D33 => c0_ddr4_adr[7] / PIN C33 => c0_ddr4_adr[5] / PIN B35 => c0_ddr4_adr[9] / PIN A33 => c0_ddr4_adr[0] / PIN A38 => c0_ddr4_adr[13] / PIN A39 => c0_ddr4_adr[11] / PIN A40 => c0_ddr4_adr[8] / PIN B40 => c0_ddr4_adr[2] / PIN C37 => c0_ddr4_ba[0] / PIN B37 => c0_ddr4_ba[1] / PIN A30 => c0_ddr4_bg[0] / PIN A34 => c0_ddr4_bg[1] / PIN D32 => c0_ddr4_cke[0] / PIN B36 => c0_ddr4_cke[1] / PIN D29 => c0_ddr4_cs_n[0] / PIN C29 => c0_ddr4_cs_n[1] / PIN K29 => c0_ddr4_dm_dbi_n[0] / PIN P26 => c0_ddr4_dm_dbi_n[1] / PIN G26 => c0_ddr4_dm_dbi_n[2] / PIN F14 => c0_ddr4_dm_dbi_n[3] / PIN E16 => c0_ddr4_dm_dbi_n[4] / PIN P15 => c0_ddr4_dm_dbi_n[5] / PIN K27 => c0_ddr4_dm_dbi_n[6] / PIN C28 => c0_ddr4_dm_dbi_n[7] / PIN H15 => c0_ddr4_dm_dbi_n[8] / PIN G28 => c0_ddr4_dq[0] / PIN F32 => c0_ddr4_dq[1] / PIN H30 => c0_ddr4_dq[2] / PIN J30 => c0_ddr4_dq[3] / PIN H28 => c0_ddr4_dq[4] / PIN J28 => c0_ddr4_dq[5] / PIN F29 => c0_ddr4_dq[6] / PIN F31 => c0_ddr4_dq[7] / PIN P23 => c0_ddr4_dq[8] / PIN N23 => c0_ddr4_dq[9] / PIN N25 => c0_ddr4_dq[10] / PIN N24 => c0_ddr4_dq[11] / PIN M23 => c0_ddr4_dq[12] / PIN L23 => c0_ddr4_dq[13] / PIN M25 => c0_ddr4_dq[14] / PIN L25 => c0_ddr4_dq[15] / PIN D28 => c0_ddr4_dq[16] / PIN F28 => c0_ddr4_dq[17] / PIN D27 => c0_ddr4_dq[18] / PIN F27 => c0_ddr4_dq[19] / PIN F25 => c0_ddr4_dq[20] / PIN E24 => c0_ddr4_dq[21] / PIN E25 => c0_ddr4_dq[22] / PIN F24 => c0_ddr4_dq[23] / PIN D14 => c0_ddr4_dq[24] / PIN C15 => c0_ddr4_dq[25] / PIN D13 => c0_ddr4_dq[26] / PIN E15 => c0_ddr4_dq[27] / PIN A14 => c0_ddr4_dq[28] / PIN B15 => c0_ddr4_dq[29] / PIN C13 => c0_ddr4_dq[30] / PIN A13 => c0_ddr4_dq[31] / PIN C18 => c0_ddr4_dq[32] / PIN D18 => c0_ddr4_dq[33] / PIN B18 => c0_ddr4_dq[34] / PIN A18 => c0_ddr4_dq[35] / PIN C16 => c0_ddr4_dq[36] / PIN B16 => c0_ddr4_dq[37] / PIN E17 => c0_ddr4_dq[38] / PIN D17 => c0_ddr4_dq[39] / PIN K16 => c0_ddr4_dq[40] / PIN K17 => c0_ddr4_dq[41] / PIN K15 => c0_ddr4_dq[42] / PIN L17 => c0_ddr4_dq[43] / PIN P16 => c0_ddr4_dq[44] / PIN M16 => c0_ddr4_dq[45] / PIN M17 => c0_ddr4_dq[46] / PIN N16 => c0_ddr4_dq[47] / PIN G25 => c0_ddr4_dq[48] / PIN H24 => c0_ddr4_dq[49] / PIN J23 => c0_ddr4_dq[50] / PIN J24 => c0_ddr4_dq[51] / PIN K26 => c0_ddr4_dq[52] / PIN H26 => c0_ddr4_dq[53] / PIN H25 => c0_ddr4_dq[54] / PIN J26 => c0_ddr4_dq[55] / PIN A24 => c0_ddr4_dq[56] / PIN C24 => c0_ddr4_dq[57] / PIN C25 => c0_ddr4_dq[58] / PIN A25 => c0_ddr4_dq[59] / PIN A28 => c0_ddr4_dq[60] / PIN C26 => c0_ddr4_dq[61] / PIN B27 => c0_ddr4_dq[62] / PIN A27 => c0_ddr4_dq[63] / PIN G17 => c0_ddr4_dq[64] / PIN F15 => c0_ddr4_dq[65] / PIN F17 => c0_ddr4_dq[66] / PIN H18 => c0_ddr4_dq[67] / PIN J18 => c0_ddr4_dq[68] / PIN G16 => c0_ddr4_dq[69] / PIN J16 => c0_ddr4_dq[70] / PIN H16 => c0_ddr4_dq[71] / PIN E29 => c0_ddr4_odt[0] / PIN A37 => c0_ddr4_odt[1] / PIN E31 => c0_sys_clk_p / PIN D31 => c0_sys_clk_n / PIN B33 => c0_ddr4_reset_n	PIN W33 => CAPI_FPGA_REFCLK_N[1] / PIN W32 => CAPI_FPGA_REFCLK_P[1] / PIN R41 => CAPI_FPGA_LANE_P[4] / PIN R42 => CAPI_FPGA_LANE_N[4] / PIN T34 => FPGA_CAPI_LANE_P[4] / PIN T35 => FPGA_CAPI_LANE_N[4] / PIN P39 => CAPI_FPGA_LANE_P[5] / PIN P40 => CAPI_FPGA_LANE_N[5] / PIN R36 => FPGA_CAPI_LANE_P[5] / PIN R37 => FPGA_CAPI_LANE_N[5] / PIN N41 => CAPI_FPGA_LANE_P[6] / PIN N42 => CAPI_FPGA_LANE_N[6] / PIN P34 => FPGA_CAPI_LANE_P[6] / PIN P35 => FPGA_CAPI_LANE_N[6] / PIN M39 => CAPI_FPGA_LANE_P[7] / PIN M40 => CAPI_FPGA_LANE_N[7] / PIN N36 => FPGA_CAPI_LANE_P[7] / PIN N37 => FPGA_CAPI_LANE_N[7] / PIN AT11 => FREERUN_CLK_P / PIN AT10 => FREERUN_CLK_N / PIN AM26 => c1_ddr4_act_n] / PIN AT26 => c1_ddr4_adr[0] / PIN AP27 => c1_ddr4_adr[1] / PIN AV27 => c1_ddr4_adr[11] / PIN AR24 => c1_ddr4_adr[12] / PIN AV24 => c1_ddr4_adr[2] / PIN AR25 => c1_ddr4_adr[3] / PIN AV26 => c1_ddr4_adr[6] / PIN AW26 => c1_ddr4_adr[7] / PIN AT28 => c1_ddr4_adr[8] / PIN AR27 => c1_ddr4_adr[9] / PIN AM28 => c1_ddr4_adr[5] / PIN AR28 => c1_ddr4_adr[13] / PIN AR23 => c1_ddr4_adr[10] / PIN AT23 => c1_ddr4_adr[4] / PIN AP24 => c1_ddr4_adr[16] / PIN AP25 => c1_ddr4_adr[14] / PIN AM24 => c1_ddr4_adr[15] / PIN AT27 => c1_ddr4_ba[0] / PIN AN27 => c1_ddr4_ba[1] / PIN AU24 => c1_ddr4_bg[0] / PIN AT25 => c1_ddr4_bg[1] / PIN AK23 => c1_ddr4_cke[0] / PIN AW27 => c1_ddr4_cke[1] / PIN AN24 => c1_ddr4_cs_n[0] / PIN AN28 => c1_ddr4_cs_n[1] / PIN AW24 => c1_ddr4_dm_dbi_n[0] / PIN AY17 => c1_ddr4_dm_dbi_n[1] / PIN AY12 => c1_ddr4_dm_dbi_n[2] / PIN AV17 => c1_ddr4_dm_dbi_n[3] / PIN AJ18 => c1_ddr4_dm_dbi_n[4] / PIN BA23 => c1_ddr4_dm_dbi_n[5] / PIN AT22 => c1_ddr4_dm_dbi_n[6] / PIN AU23 => c1_ddr4_dm_dbi_n[7] / PIN AM19 => c1_ddr4_dm_dbi_n[8] / PIN BB24 => c1_ddr4_dq[0] / PIN AY25 => c1_ddr4_dq[1] / PIN BB25 => c1_ddr4_dq[2] / PIN BA25 => c1_ddr4_dq[3] / PIN AY27 => c1_ddr4_dq[4] / PIN AY28 => c1_ddr4_dq[5] / PIN BA28 => c1_ddr4_dq[6] / PIN BB28 => c1_ddr4_dq[7] / PIN BA13 => c1_ddr4_dq[8] / PIN AY14 => c1_ddr4_dq[9] / PIN BA16 => c1_ddr4_dq[10] / PIN BB16 => c1_ddr4_dq[11] / PIN BB13 => c1_ddr4_dq[12] / PIN AY15 => c1_ddr4_dq[13] / PIN AW17 => c1_ddr4_dq[14] / PIN AW16 => c1_ddr4_dq[15] / PIN BB11 => c1_ddr4_dq[16] / PIN BA10 => c1_ddr4_dq[17] / PIN AV14 => c1_ddr4_dq[18] / PIN BB10 => c1_ddr4_dq[19] / PIN AU14 => c1_ddr4_dq[20] / PIN AW14 => c1_ddr4_dq[21] / PIN BA11 => c1_ddr4_dq[22] / PIN AW15 => c1_ddr4_dq[23] / PIN AT16 => c1_ddr4_dq[24] / PIN AU15 => c1_ddr4_dq[25] / PIN AU18 => c1_ddr4_dq[26] / PIN AR17 => c1_ddr4_dq[27] / PIN AT17 => c1_ddr4_dq[28] / PIN AU16 => c1_ddr4_dq[29] / PIN AV18 => c1_ddr4_dq[30] / PIN AT15 => c1_ddr4_dq[31] / PIN AN16 => c1_ddr4_dq[32] / PIN AM16 => c1_ddr4_dq[33] / PIN AN18 => c1_ddr4_dq[34] / PIN AL16 => c1_ddr4_dq[35] / PIN AM18 => c1_ddr4_dq[36] / PIN AN17 => c1_ddr4_dq[37] / PIN AL18 => c1_ddr4_dq[38] / PIN AP16 => c1_ddr4_dq[39] / PIN BA18 => c1_ddr4_dq[40] / PIN BB19 => c1_ddr4_dq[41] / PIN BB18 => c1_ddr4_dq[42] / PIN BA21 => c1_ddr4_dq[43] / PIN BA22 => c1_ddr4_dq[44] / PIN BB20 => c1_ddr4_dq[45] / PIN AY22 => c1_ddr4_dq[46] / PIN AY23 => c1_ddr4_dq[47] / PIN AT20 => c1_ddr4_dq[48] / PIN AU19 => c1_ddr4_dq[49] / PIN AR19 => c1_ddr4_dq[50] / PIN AR20 => c1_ddr4_dq[51] / PIN AP20 => c1_ddr4_dq[52] / PIN AP22 => c1_ddr4_dq[53] / PIN AP19 => c1_ddr4_dq[54] / PIN AN22 => c1_ddr4_dq[55] / PIN AW20 => c1_ddr4_dq[56] / PIN AV19 => c1_ddr4_dq[57] / PIN AU20 => c1_ddr4_dq[58] / PIN AW19 => c1_ddr4_dq[59] / PIN AW22 => c1_ddr4_dq[60] / PIN AU21 => c1_ddr4_dq[61] / PIN AV21 => c1_ddr4_dq[62] / PIN AV22 => c1_ddr4_dq[63] / PIN AM21 => c1_ddr4_dq[64] / PIN AK22 => c1_ddr4_dq[65] / PIN AL22 => c1_ddr4_dq[66] / PIN AM20 => c1_ddr4_dq[67] / PIN AJ20 => c1_ddr4_dq[68] / PIN AL21 => c1_ddr4_dq[69] / PIN AJ21 => c1_ddr4_dq[70] / PIN AJ22 => c1_ddr4_dq[71] / PIN AN26 => c1_ddr4_odt[0] / PIN AU28 => c1_ddr4_odt[1] / PIN AU25 => c1_sys_clk_p / PIN AU26 => c1_sys_clk_n / PIN AV28 => c1_ddr4_reset_n] / PIN AK20 => c1_ddr4_dqs_t[8] / PIN AK19 => c1_ddr4_dqs_c[8] / PIN BA26 => c1_ddr4_dqs_t[0] / PIN BB26 => c1_ddr4_dqs_c[0] / PIN AJ17 => c1_ddr4_dqs_t[4] / PIN AK17 => c1_ddr4_dqs_c[4] / PIN AR18 => c1_ddr4_dqs_t[3] / PIN AT18 => c1_ddr4_dqs_c[3] / PIN AY19 => c1_ddr4_dqs_t[7] / PIN AY18 => c1_ddr4_dqs_c[7] / PIN AN21 => c1_ddr4_dqs_t[6] / PIN AP21 => c1_ddr4_dqs_c[6] / PIN AU13 => c1_ddr4_dqs_t[2] / PIN AV13 => c1_ddr4_dqs_c[2] / PIN AM23 => c1_ddr4_ck_t[0] / PIN AN23 => c1_ddr4_ck_c[0] / PIN AY20 => c1_ddr4_dqs_t[5] / PIN BA20 => c1_ddr4_dqs_c[5] / PIN BA15 => c1_ddr4_dqs_t[1] / PIN BB15 => c1_ddr4_dqs_c[1]

## Clocking
Two DDR4 memory interface IP each gets 120Mhz reference clock from on board clock generator . The Mixed-Mode Clock Manger (MMCM) inside the IP generates the 1066Mhz memory interface clock and 266Mhz for two user interface logic blocks. These two 266Mhz clocks are coming from two different MMCM and therefore they are considered as asynchronous from each other.
Xilinx GTY transceiver gets 133.33Mhz reference clock from DDIMM connector and MMCM generates the clock for 21.33Ghz or 25.6Ghz OpenCAPI link. The MMCM also generates divided by 64 clock (333Mhz or 400Mhz) for ICE core logic.
ICE pervasive logic (JTAG) runs at 66.5Mhz frequency and uses the 133Mhz reference clock from the on board clock generator.
## Reset
ICE received active low reset from DDIMM connector. De-assertion of reset triggers Xilinx GTY transceiver initialization. GTY RX initialization takes about 24us to complete and ICE core logic is held in reset during this time frame. Once RX initialization completed, ICE core logic is out of reset. Xilinx DDR4 IP doesn’t get reset during this time frame. If the DDR4 calibration failed during the programming of the FPGA, then DDR4 IP gets reset from calibration retry logic.
## Memory Initialization & Calibration
### Calibration
Xilinx PHY performs internal calibration after initial programming or after system reset asserted to the memory IP. PHY indicates calibration completion status and memory controller begins issuing commands to the memory. Please refer to UltraScale FPGAs Memory IP (xilinx_mc.pdf) for detailed calibration process. If calibration failed, ICE kicks off memory re-calibration by asserting reset to Memory IP. Calibration status are posted in ICE Trap Register 4.
### Memory Initialization
ICE supports basic memory initialization. ICE can initialize the entire 32GB of memory space with data of 0 or initialize with data equal to address on a 64B granularity. User needs to kick off the memory initialization sequence through ICE Configuration Register 1. ICE memory initialization unit doesn’t perform any type of fencing or quiesce. It is up to the user to ensure that memory calibration is completed and no memory operations are pending before start the memory initialization. Memory initialization status are posted in ICE Trap Register 4.
## JTAG
The ICE pervasive allows limited register access via JTAG, and interacts with specific firmware procedures sent by the host. The JTAG utilizes the Xilinx IP in order for us to read incoming data via an AXI-LITE interface. ICE doesn’t have a complete AXI bus connecting the pervasive logic to the register’s so accesses are limited. The available registers are listed in the figure below for the 32-bit JTAG registers.

## Xilinx GTY transceivers

Figure 1: ICE Pervasive Register Access
   Refer to Xilinx UltraScale Architecture GTY Transceivers User Guide
## OpenCAPI DLx
   Refer to Date Link Layer Specification
## OpenCAPI TLx
  Refer to TLX 31. OMI Reference Design
## Error Report and Interrupt Handling
### Functional Description
Handles basic error reporting on ICE Platform and handles packing interrupt requests for transmission to the host.
### Interfaces

Signal Name	I/O	Size	Description	Async
ice_errrpt_err_bus	I		All errors coming in from other units in the ICE Logic. Size/Scope TBD.
Interface with MMIO
mmio_errrpt_intrp_hdl_xstop	I	64	Object handle used for channel checkstop interrupt.
mmio_errrpt_intrp_hdl_app	I	64	Object handle used for application interrupt
mmio_errrpt_intrp_flag_xstop	I	4	Command flag used for channel checkstop interrupt
mmio_errrpt_intrp_flag_app	I	4	Command flag used for application interrupts.
Interface with CFG
cfg_tlx_function_actag_base	I	12	Function 0 actag base. Used as the single actag used by ICE. Should be same as afu actag, if not this will be considered an error.
cfg_tlx_function_actag_len_enab	I	12	Function 0 actag length enable. Should indicate length of 1. Any other value will be viewed as an error
cfg_tlx_afu_actag_base	I	12	AFU actag base. Used as the single actag used by ICE. Should be same as function actag, if not this will be considered an error.
cfg_tlx_afu_actag_len_enab	I	12	Afu actag length enable. Should indicate length of 1.Any other value will be considered an error.
Response Interface with TLX
afu_tlx_resp_initial_credit	O	7	Specifies initial credits for sending CAPP responses to the AFU. Constant set to 4.
afu_tlx_resp_credit	O	1	CAPP Response credit return. Indicates that AFU can not accept another response from the TLX.
tlx_afu_resp_valid	I	1	Response valid on this cycle
tlx_afu_resp_opcode	I	8	Response opcode
tlx_afu_resp_afutag	I	16	Response AFU Tag

Command Interface with TLX
tlx_afu_cmd_initial_credit	I	4	Initial credit to load AFU command credit counter.
tlx_afu_cmd_credit	I	1	AFU can send another command to the TLX. / Decrement credit counter when command is sent, increment with this signal.
afu_tlx_cmd_valid	O	1	Indicates that a valid VC3 command is pending in errrpt logic.
afu_tlx_cmd_opcode	O	8	Opcode for pending command.
afu_tlx_cmd_actag	O	12	AC Tag
afu_tlx_cmd_stream_id	O	4	Stream ID
afu_tlx_cmd_ea_or_obj	O	64	Object handle. ICE does not support upstream commands using effective address (EA)
afu_tlx_cmd_afutag	O	16	AFU Tag
afu_tlx_cmd_flag	O	4	Command flag
afu_tlx_cmd_bdf	O	16	Bus Device Function
afu_tlx_cmd_pasid	O	20	PASID

### Error

Err0 Bit	Err0 Bit / (LE)	Unit	Description
0	63	TLX_rcv	DLX supplying valid and error in the same cycle
1	62	TLX_rcv	Data flit runlength more than 8
2	61	TLX_rcv	Input fifo overflowed
3	60	TLX_rcv	Input fifo underflowed
4	59	TLX_rcv	Unexpected collision between start_ctl and write data
5	58	TLX_rcv	Cmd good data count underflow
6	57	TLX_rcv	Cmd good data count overflow
7	56	TLX_rcv	Data steering fifo underflowed
8	55	TLX_rcv	Data steering fifo overflowed
9	54	TLX_rcv	Response fifo underflowed
10	53	TLX_rcv	Response fifo overflowed
11	52	TLX rcv	Command data fifo underflowed
12	51	TLX rcv	Command data fifo overflowed
13	50	TLX rcv	Invalid value supplied on afu_tlx_cmd_rd_cnt
14	49	TLX rcv	Array overflow in input fifo
15	48	TLX rcv	Command fifo underflowed
16	47	TLX rcv	Command fifo overflowed
17	46	TLX rcv	Config fifo underflowed
18	45	TLX rcv	Config fifo overflowed
19	44	TLX rcv	Config data fifo overflowed
20	43	TLX rcv	Config data fifo underflowed
21	42	TLX rcv	Bad template – (not 0 or 1 or 4)
22	41	TLX rcv	Bad length for MMIO read or write (length must be 8 bytes)
23:31	40:32	TLX rcv	TBD
32	31	AFU Main	Cmd FIFO overflow
33	30	AFU Main	Cmd FIFO underflow
34	29	AFU Main	Write data Control FIFO overflow
35	28	AFU Main	Write data Control FIFO underflow
36	27	AFU Main	MMIO response and DRAM response request received same cycle
37	26	AFU Main	Response Credit counters exceeded Initial Credit
38	25	AFU Main	AFU received unexpected write data
39	24	AFU Main	CMD control parity error
40	23	AFU Main	Max Asynchronous FIFO credit exceeded
41	22	AFU Main	AFU received unsupported commands from TLX
42	21	AFU Main	Response credit counter underflow
43	20	AFU Main	AFU received command with unsupported Data Length
44:47	19:16	AFU Main	TBD
48	15	TLX xmt	TLX Credit Overflow
49	14	TLX xmt	Hardware Shift Error
50	13	TLX xmt	Metadata Fifo Overflow
51	12	TLX xmt	Metadata Fifof Underflow
52	11	TLX xmt	DCP0 Data Fifo Overflow
53	10	TLX xmt	DCP0 Data Fifo Underflow
54	9	TLX xmt	VC3 cmd Fifo Overflow
55	8	TLX xmt	VC3 cmd Fifo Underflow
56	7	TLX xmt	VC0 resp Fifo Overflow
57	6	TLX xmt	VC0 resp Fifo Underflow
58	5	TLX xmt	Meta Packet Ptr Over Max
59	4	TLX xmt	Rogue Response Data Error
60	3	TLX xmt	Read attempted with metadata enabled but no template which supports metadata
61	2	TLX xmt	Response Data Missing
62	1	Ice Regs	Control Register Parity Error
63	0	Ice Regs	Informational Register Parity Error

## MMIO
### Functional Description
Logic used to mimic OCMB MMIO space on the ICE platform. A number of select registers are implemented to provide firmware support and facilitate certain function needed by the platform. MMIO commands are sourced from the command decode/address xlate block, and responses are presented to arbitration logic feeding the TLX framer.
### Interfaces

Signal Name	I/O	Size	Description	Async
xlate_mmio_cmd_val	I	1	Indicates that xlat_mmio_cmd_* inputs are valid this cycle. MMIO request pending	No
mmio_xlate_fc	O	1	Staged Read signal from mmio fifo.	NO
xlate_mmio_cmd_addr	I	35	Address targeted by the MMIO read.
xlate_mmio_cmd_rd	I	1	Request Direction. (1=rd, 0=wr)
xlate_mmio_cmd_tag	I	16	CAPP Tag associated with the request.
xlate_mmio_cmd_plen	I	3	Partial Length / This field should only ever be 0b011 to indicate that the partial length is 8 bytes. However: / For reads, encodings of 0b000, 0b001 and 0b010 to indicate partial lengths of 1, 2 and 4 byte respectively will result in the return of eight bytes. Any other encodings will result in read fail with “unsupported operand length” response code. / For writes, any encodings other than 0b011 will result in write fail with “unsupported operand length” response code. / **internally drive to 8B
xlate_mmio_cmd_par	I	1	Even parity on xlat_mmio_cmd_* signals optional
xlate_mmio_data	I	512	MMIO Data Bus. Feed full data flit, mmio will parse out correct command data or could move this to the command decode block.
xlate_mmio_data_val	I	1	Data is valid this cycle. Separate from command valid.
Interface to Interupt Handler
mmio_errrpt_intrp_hdl_xstop	O	64	Object handle used for channel checkstop interrupt.
mmio_errrpt_intrp_hdl_app	O	64	Object handle used for application interrupt
mmio_errrpt_intrp_flag_xstop	O	4	Command flag used for channel checkstop interrupt
mmio_errrpt_intrp_flag_app	O	4	Command flag used for application interrupts.
Interface to VC0 Mux
mmio_afu_resp_val	O	1	MMIO response pending. Indicates that all mmio_arb_resp* interfaces are valid this cycle. Asserted until arb_mmio_resp_ack is asserted.
afu_mmio_resp_ack	I	1	ACK from vc0 arbiter to MMIO.
mmio_afu_resp_tag	O	16	CAPP Tag associated with the pending response.
mmio_afu_resp_opcode	O	8	CAPI Opcode associated with the response.
mmio_afu_resp_dl	O	2	Data Length for the current response. Constant at b01 (64B)
mmio_afu_resp_dp	O	2	Data part associated with the current mmio response. Will be constant at b00. (Offset at 0 bytes) / Note: This interface will need to change if support for 32B carriers is added.
mmio_afu_resp_code	O	4	Response code associated with the current response. / - 0000 for successful reads/writes
mmio_afu_rdata_bus	O	512	MMIO Data Bus

## AFU Main
AFU Main decodes command from TLX parser and pushes into the 8-entry deep command buffer. Command credit is returned to TLX parser once a command is removed from the command buffer. AFU main only accepts mem_rd, mem_write, partial mem_rd and partial mem_wr commands. An error is reported if unsupported command is received.
A Config Write to bit 1 of OpenCAPI Function 1 Memory Space Enable Register is needed to Enable MMIO BAR Memory space. If enable bit is not set, any partial ops to AFU Main would turns into 64B memory access. Any partial ops to region outside the MMIO BAR would also turns into 64B memory access if enable bit is set.

There are flow control mechanisms between AFU main and each port of memory user interface as well as between AFU main and MMIO unit. There are 4 credits for MMIO commands. Each memory port has 256 credits for read and 256 credits for write. Command flows out of the command buffer in FIFO order to either memory port 0, memory port 1 or MMIO unit. The command FIFO pauses if the credit for the head of command buffer command isn’t available.
Address translation is done at AFU main to allow maximum performance at DDR4 interface. Refer to Address Re-mapper table in ICE Memory Interface section for detailed host to memory controller address translation.
AFU Main requests data from TLX parser once command is forwarded to the memory user interface. Data steering logic retrieves data control signals from the write data control fifo once data from TLX parser has arrived. Data steering logic determines if data goes to memory port 0, memory port 1 or MMIO unit.
AFU Main handles responses from memory ports and MMIO unit. Once TLX framer indicated credit for the corresponding response is available, AFU Main pushes response command or response data to TLX framer. In the case where both MMIO and memory ports both want to send the response back, yield signal is raised to memory port and allow MMIO response to use the response channel first.
## ICE Memory Interface

Figure 2: ICE MCI High Level Design.

### Primary Interfaces
Table 1: Primary Interface
Port	Description
Clocks and Utility
i_reset	Primary Reset. Reset all flow control to 256 read / 256 write buffer requests. / Must be held for at least 40 nsec while both i_hclk and i_mclk are running / i_cmd_valid must be held low for at least 40 nsec after i_reset is deasserted to allow the reset to propagate through the metastability stages.
i_hclk	Host Clock (400Mhz)
i_mclk(1:0)	Memory Clock (266 Mhz). Must be div 4 of Memory Interface SDR clock. / (0) : Port 0 / (1) : Port 1
o_idle(1:0)	Idle indicator. Indicates whether MC0 or MC1 are idle (=1) of any operations. Sync to HCLK. / 0: MC0. / 1: MC1.
o_mc0_fifo_err(9:0) / o_mc1_fifo_err(9:0)	Fifo Error (=1). all sync to Hclk. / 0 : WD Fifo, Host Side 5: WD Fifo MCtrl Side / 1 : CM Fifo, Host Side 6 : CM Fifo MCtrl Side / 2 : RD Fifo, MCtrl Side 7 : RD Fifo Host Side / 3 : RS Fifo, MCtrl Side 8 : RS Fifo Host Side / 4 : WS Fifo, MCtrl Side 9 : WS Fifo Host Side
Host Interface Command Interface / all these signals are synchronous to i_hclk
i_cmd_valid	0: No Op / 1 : i_rw, i_addr, i_tag and i_size is valid / Each command consumes one credit from the respective credit pool ( wr/rd , intlv0/1 ) / There are a total of 256 read and 256 write credits per interleave. Each credit uses 128B of data. / (this sizing was chosen to optimize the use of a 36K Xilinx RAM).
i_cmd_rw	0 : read (from dram) / 1 : write (to dram)
i_cmd_addr(31:3	MCI Address. See Table 2. / i_cmd_addr(31) determines which interleave the credit should be deducted from. / Note, these are 8B addresses
i_cmd_tag(15:0)	tag associated with i_cmd. Returned with write done or read response / The interface does not interpret this field. It will be passed back with the corresponding read or write response.
i_cmd_size	0: 64B / 1: 128B
i_wvalid(1:0)	Request to send 64B line of write data via i_wdata. / Writes data must be pushed in the order the request were made on i_cmd_valid / 00 : No request / 10: Request to Interleave 1 / 01: Request to Interleave 0 / 11: Multicast to both interleaves. / Data must be moved coincident or subsequent to the corresponding i_cmd_valid and may not be made if there was no credit for that write command.
i_wdata(511:0) / i_wmeta(39:0)	64B of write data and 5 Bytes of Meta data. Parity per section 1.17.4 will be generated and written to memory using 8 continous burst beats in the dram. i_wdata and i_wmeta are valid same cycle as i_wvalid. Offset 0 must come first. If 128B write, the second offset must come before data from a subsequent command is serviced.
i_yield(1:0)	(0): Yield read response / (1): Yield write reponse. / Assert (=1) to inhibit arbiter from picking specific type of response. Used for system to gain control of the response mux. Selecting both signals inhibits all responses. / Arbiter stops processing requests 2 cycles after respective signal is asserted. / Note this will eventually back up the command bus.
i_arbwt(7:0)	(1:0) Weight for o_cmd_fc(0) / (3:2) Weight for o_cmd_fc(1) / (5:4) Weight for o_cmd_fc(2) / (7:6) Weight for o_cmd_fc(3) / Weight encoding : / "00" => 1 request; "01" => 2 requests; "10" => 3 requests; "11" => 4 requests / May be dynamically changed.
Host Responses / all these signals are synchronous to i_hclk
o_cmd_fc(3:0)	Response Valid / Command flow control Return. (=1) decoded as follows. / 0 : return of credit, write intlv 0 (write done, intlv 0) / 1 : return of credit, write intlv 1 (write done, intlv 1) / 2 : return of data, read intlv 0 / 3: return of data, read intlv 1 / read credit calculated by qualifying o_cmd_fc(2,3) with the following condition : / ( o_rsp_size xnor o_rsp_offs )
o_rsp_tag(15:0)	Read response or Write done tag. valid with o_cmd_fc. corresponds to original request.
o_rsp_offs / o_rsp_size / o_rsp_data(511:0) / o_rsp_meta(39:0)	read response offset, size and data Valid with o_cmd_fc(2,3) / The start of the response is qualified by offs=0. The credit is qualified when size=0, offs=0 or size=1 offs=1 and when o_cmd_fc(2,3) is 1. / write response tag is valid with o_cmd_fc(0,1). Size is also valid if needed. offs, data and meta are not valid.
o_rsp_perr(23:0)	indicates a calculated parity error in the respective dimension on the read response qualified by o_cmd_fc(2,3) / (23:16) : pin / (15:8) : chip / (7:0) : line
Memory Controller Interface / port 0 is synchronous to i_mclk(0), port 1 is synchronous to i_mclk(1)
-- port 0 / i_ddr0_mc0_app_rdy / i_ddr0_mc0_app_wdf_rdy / i_ddr0_mc0_app_rd_data_end / i_ddr0_mc0_app_rd_data_valid / i_ddr0_mc0_app_rd_data / o_mc0_ddr0_addr / o_mc0_ddr0_cmd / o_mc0_ddr0_en / o_mc0_ddr0_wdf_end / o_mc0_ddr0_wdf_wren / o_mc0_ddr0_wdf_data / -- port 1 / i_ddr1_mc1_app_rdy / i_ddr1_mc1_app_wdf_rdy / i_ddr1_mc1_app_rd_data_end / i_ddr1_mc1_app_rd_data_valid / i_ddr1_mc1_app_rd_data / o_mc1_ddr1_addr / o_mc1_ddr1_cmd / o_mc1_ddr1_en / o_mc1_ddr1_wdf_end / o_mc1_ddr1_wdf_wren / o_mc1_ddr1_wdf_data	These signals connect directly to the Xilinx Memory Controller. / Port 0 is the even interleave.

### Address Remapper
Prior to posting the address to the MCI, the OC System Address must be remapped to the MCI (internal) address better utilize the Controller. The controller maintains 4 ordered queues mapped to the Bank Group. There are two controllers, selected by the interleave bit.

Table 2: Address Remapping
OC Effective	MCI Address / (i_cmd_addr)	DRAM Designation	Comments
5:3	2:0	Col(2:0)	BL=8, minimum 64B per request. Must be tied to 0.
8,6	4:3	BG(1:0)	(want 128B Line in one interleave)
10:9	6:5	BA(1:0)
11	7	Col(3)	full cacheline in one interleave.
32:31, 15:12	13:8	Col(9:4)
33, 30:16	29:14	Row(15:0)
34	30	Rank(0)
7	31	Port Interleave	(Must be >=7). 7 interleaves cachelines between ports.
2:0	x	Chip(2:0)	minimum 8B per line.

Other considerations about the addressing

- To insure the two parts of a cacheline (128B) stays ordered, the line must be in the same interleave.
- Reads and writes to the same address remain ordered
- Reads and writes to the same bank group remain ordered.
- Reads and writes outside of the bank group are not in anyway ordered.

### Flow Control
The command interface into the MCI uses flow control partitioned by command type and interleave. There are 256 Read request buffers and 256 Write Request Buffers for each port interleave. A credit (1 request) covers both 1 and 2 beat requests.

Prior to issuing i_cmd_valid, the user must internally decrement one credit from the pool corresponding to the cmd and interleave. If there is enough credit the command (and write data if relevant) may be sent

The credit for the respective command and interleave is returned on o_cmd_fc when either the write done is posted or the read response data is ready. One credit is returned regardless of the size of the data.

The user interface can halt the response interface by asserting the yield signal. The interface will be idle in 2 cycles.

The user resets it's credit to a maximum of 256/256 with an assertion of i_reset.
### Parity Scheme
Data is protected on a 64B block based by calculating 8 even parity bits across 3 dimensions
1. Chip (1 parity for the 8 burst lines across the 8 pins per chip)
2. Line (1 parity for each line running across all 8 pins across all 8 chips)
3. Pin (1 parity for each pin running across all 8 lines across all 8 chips)

Formally,
Figure 3: Parity Cube

for L = 0 to 7 {	-- Line
  for C = 0 to 7 {	-- Chip
     for P = 0 to 7 {	-- Pin
       A(L,C,P) = Data(64*L + 8*C + P)
}}}

for x = 0 to 7 {
    Line_p(x) = 0
    Chip_p(x) = 0
    Pin_p(x) = 0
  for y = 0 to 7 {
    for z = 0 to 7 {
       Line_p(x) ^= A(x,y,z)
Chip_p(x) ^= A(y,x,z)
Pin_p(x) ^= A(y,z,x)
}}}

Furthermore, the 9th DRAM (C=8) is then defined to contain

for L= 0 to 7 {
  for P=0 to 7 {
    A(0,8,P) <= Pin_p(P)
    A(1,8,P) <= Chip_p(P)
    A(2,8,P) <= Line_p(P)
    A(3,8,P) <= Meta(P)
    A(4,8,P) <= Meta(8+p)
    A(5,8,P) <= Meta(16+p)
    A(6,8,P) <= Meta(24+p)
    A(7,8,P) <= Meta(32+p)
}}

### Interface to Memory Controller
The System connects to the DRAM via 2 instantiations of a Xilinx integrated Memory Controller. This controller provides a 4:1 data interface to 1066 Mhz DDR arranged in a line of 9 dual-rank x8 chips providing for a BL8 burst of 8 x 72 bits. This enables a sustained data rate of 576bits (72B) per cycle at 1066Mhz which is 19GB/sec per port.

There are 2 memory controller interfaces, each supporting 72B apiece. Access to a port is decoded by the port interleave bit which can be remapped to any one of the system address bits.

Figure 4: ICE MCI High Level Design.
### Ordering
Read and write requests to the same memory location are never reordered (controlled by imported IP; cannot be changed).

Read and write request to the same address mapped to the Bank Group on the memory controller are never reordered.

Read and write requests to different bank groups are processed in whatever order satisfies the memory timing contstraints.

There is no ordering between read or writes to different port interleaves. The large command buffer size allows enough look ahead to insure that both interleaves are active.

### Memory Timing controls
AutoPrechage is not used.

Self-Refresh is not done.

The Xilinx memory controller controls all scheduling of refreshes and precharges. These will appear as momentary wait states on the command bus should they result in backpressure.
## Xilinx Memory Controller IP
        Refer to Xilinx UltraScale FPGAs Memory IP

## Supported Memory Topologies

Figure 5: DDR4 Controller IP basic options
- 16GB per port with total of 32GB
- 2 Ranks per port
- 8G per rank
- 9 devices per port total 18 devices
- Micro Twin Die x8 (2x 8Gb die)
- 72b wide per channel
## Registers
### Registers overview

Mnemonic	Address Offset	Name
AFU_MAC.CFG.ICE0DID	0x00000000	OpenCAPI Function 0 Device ID & Vendor ID Register
AFU_MAC.CFG.ICE0SYID	0x0000002c	OpenCAPI Function 0 MMIO Subsystem ID & Subsystem Vendor ID Register
AFU_MAC.CFG.ICE1BARH	0x00010014	OpenCAPI Function 1 MMIO Base Upper Address 0 Register
AFU_MAC.CFG.ICE1BARL	0x00010010	OpenCAPI Function 1 MMIO Base Upper Address 0 Register
AFU_MAC.CFG.ICE1DID	0x00010000	OpenCAPI Function 0 Device ID & Vendor ID Register
AFU_MAC.CFG.ICE1MBIT	0x00010004	OpenCAPI Function 1 Memory Space Enable Register
AFU_MAC.CFG.ICE1SYID	0x0001002c	OpenCAPI Function 1 MMIO Subsystem ID & Subsystem Vendor ID Register
AFU_MAC.CFG.ICEAFUEN	0x0001050c	OpenCAPI AFU Control DVSEC AFU Enable and ID Register
AFU_MAC.CFG.ICEATAGB	0x0001051c	OpenCAPI AFU Control DVSEC acTAG Register
AFU_MAC.CFG.ICEATAGL	0x00010518	OpenCAPI AFU Control DVSEC acTAG Length Register
AFU_MAC.CFG.ICEFTAG	0x0001030c	OpenCAPI Function acTAG Register
AFU_MAC.CFG.ICEPIDB	0x00010514	OpenCAPI AFU Control DVSEC PASID Base Register
AFU_MAC.CFG.ICEPIDL	0x00010510	OpenCAPI AFU Control DVSEC PASID Length Register
AFU_MAC.CFG.ICERCAP	0x0000021c	OpenCAPI TLX Receive Template 31-0 Capabilities Register
AFU_MAC.CFG.ICERRATE	0x0000024c	OpenCAPI TLX Flit Receive Rate per Template 7-0 Capabilities Register
AFU_MAC.CFG.ICETCFG	0x00000224	OpenCAPI TLX Transmit Template Configurations Register
AFU_MAC.CFG.ICETRATE	0x0000026c	OpenCAPI TLX Flit Transmit Rate per Templates 7-0 Configurations Register
AFU_MAC.CFG.ICEVER	0x00000210	OpenCAPI Transport Layer Configuration Register
AFU_MAC.MMIO.ICE_REGS.ICECFG0	0x0801240c	ICE Configuration Register 0
AFU_MAC.MMIO.ICE_REGS.ICECFG1	0x0801240d	ICE Configuration Register 1
AFU_MAC.MMIO.ICE_REGS.ICECFG2	0x0801240e	ICE Configuration Register 2
AFU_MAC.MMIO.ICE_REGS.ICEINTHLD0	0x08012410	ICE Interrupt Handle Register 0
AFU_MAC.MMIO.ICE_REGS.ICEINTHLD1	0x08012411	ICE Interrupt Handle Register 1
AFU_MAC.MMIO.ICE_REGS.ICEINTHLD2	0x08012412	ICE Interrupt Handle Register 2
AFU_MAC.MMIO.ICE_REGS.ICEINTHLD3	0x08012413	ICE Interrupt Handle Register 3
AFU_MAC.MMIO.ICE_REGS.ICETRAP0	0x08012424	ICE Trap Register 0
AFU_MAC.MMIO.ICE_REGS.ICETRAP1	0x08012425	ICE Trap Register 1
AFU_MAC.MMIO.ICE_REGS.ICETRAP2	0x08012426	ICE Trap Register 2
AFU_MAC.MMIO.ICE_REGS.ICETRAP3	0x08012427	ICE Trap Register 3
AFU_MAC.MMIO.ICE_REGS.ICETRAP4	0x08012428	ICE Trap Register 4
AFU_MAC.MMIO.ICE_REGS.ICETRAP5	0x08012429	ICE Trap Register 5
AFU_MAC.MMIO.ICE_REGS.ICETRAP6	0x0801242a	ICE Trap Register 6
AFU_MAC.MMIO.ICE_REGS.ICETRAP7	0x0801242b	ICE Trap Register 7
AFU_MAC.MMIO.ICE_REGS.ICETRAP8	0x0801242c	ICE Trap Register 8
AFU_MAC.MMIO.ICE_REGS.ICE_ERR0_REPORTQ	0x0801241c	ICE Error report register 0
AFU_MAC.MMIO.ICE_REGS.ICE_ERR0_REPORTQ_MASK	0x08012414	ICE ERROR Report Mask Register 0
AFU_MAC.MMIO.ICE_REGS.ICE_ERR1_REPORTQ	0x0801241d	ICE Error report register
AFU_MAC.MMIO.ICE_REGS.ICE_ERR1_REPORTQ_MASK	0x08012415	ICE ERROR Report Mask Register 1
AFU_MAC.MMIO.ICE_REGS.ICE_ERR2_REPORTQ	0x0801241e	ICE Error report register
AFU_MAC.MMIO.ICE_REGS.ICE_ERR2_REPORTQ_MASK	0x08012416	ICE ERROR Report Mask Register 1

### ICE Register Descriptions

Mnemonic	AFU_MAC.CFG.ICE0DID
Name	OpenCAPI Function 0 Device ID & Vendor ID Register
Reset Value	0x06361014
Description	OpenCAPI Device ID and Vendor ID Register for Function 0
VHDL	Value
Name	0b00000, 0b00, 0b000, 0b00, 0b0, 0b00, 0b0000, 0b0, 0b0000000, 0b0, 0b0, 0b0, 0b00
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00000000
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:0	0x06361014	RESERVED	RO	constant=0b00000110001101100001000000010100

Mnemonic	AFU_MAC.CFG.ICE0SYID
Name	OpenCAPI Function 0 MMIO Subsystem ID & Subsystem Vendor ID Register
Reset Value	0x06361014
Description	Function 0 Subsystem ID and Subsystem Vendor ID
VHDL	Value
Name	0b00000, 0b00, 0b000, 0b00, 0b0, 0b00, 0b0000, 0b0, 0b0000000, 0b0, 0b0, 0b0, 0b00
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0000002c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:0	0x06361014	RESERVED	RO	constant=0b00000110001101100001000000010100

Mnemonic	AFU_MAC.CFG.ICE1BARH
Name	OpenCAPI Function 1 MMIO Base Upper Address 0 Register
Reset Value	0xFFFFFFF8
Description	Indicates the MMIO Base Address for window 0, Function 1. This is used to access MMIO registers.
VHDL	Value
Name	AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(31), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(30), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(29), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(28), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(27), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(26), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(25), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(24), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(23), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(22), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(21), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(20), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(19), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(18), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(17), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(16), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(15), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(14), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(13), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(12), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(11), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(10), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(9), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(8), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(7), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(6), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(5), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(4), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_014_q(3), 0b000
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00010014
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:3	0x1fffffff	ICE1BARH_BAR_ADDRESS	RW	Upper 29 bits for Base Address for window. The window is 32GB in size so the lower 35 bits of the base address is zero. This field is disruptive to write during runtime.
2:0	0x0	RESERVED	RO	constant=0b000

Mnemonic	AFU_MAC.CFG.ICE1BARL
Name	OpenCAPI Function 1 MMIO Base Upper Address 0 Register
Reset Value	0x00000004
Description	Indicates the MMIO Base Address for window 0, Function 1. This is used to access MMIO registers.
VHDL	Value
Name	0b0000000000000000000000000000, AFU_MAC.CFG.CFG.CFG_F1.reg_csh_010_q(3), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_010_q(2), AFU_MAC.CFG.CFG.CFG_F1.reg_csh_010_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00010010
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:4	0x0	RESERVED	RO	constant=0b0000000000000000000000000000
3	0x0	ICE1BARL_PREFETCHABLE	RO	This field is 0 to indicate the window is not prefetchable. RO from OC config space.
2:1	0x2	ICE1BARL_TYPE	RO	This field is set to 0b10 to indicate 64-bit addressing. RO from OC config space.
0	0x0	ICE1BARL_ADDRESS_SPACE	RO	This field is set to 0 to indicate this is a Memory Address Space. RO from OC config space.

Mnemonic	AFU_MAC.CFG.ICE1DID
Name	OpenCAPI Function 0 Device ID & Vendor ID Register
Reset Value	0x06361014
Description	OpenCAPI Device ID and Vendor ID Register for Function 1
VHDL	Value
Name	0b00000, 0b00, 0b000, 0b00, 0b0, 0b00, 0b0000, 0b0, 0b0000000, 0b0, 0b0, 0b0, 0b00
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00010000
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:0	0x06361014	RESERVED	RO	constant=0b00000110001101100001000000010100

Mnemonic	AFU_MAC.CFG.ICE1MBIT
Name	OpenCAPI Function 1 Memory Space Enable Register
Reset Value	0x00100000
Description	OpenCAPI Function 1 Memory Space Enable Register
VHDL	Value
Name	0b00000000000, AFU_MAC.CFG.CFG.CFG_F1.reg_csh_004_q(20), 0b000000000000000000, AFU_MAC.CFG.CFG.CFG_F1.reg_csh_004_q(1), 0b0
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00010004
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:21	0x0	RESERVED	RO	constant=0b00000000000
20	0x1	ICE1MBIT_CAPABILITIES_LIST	RO	Capabilities list pointer supported = 1
19:2	0x0	RESERVED	RO	constant=0b000000000000000000
1	0x0	ICE1MBIT_MEMORY_SPACE	RW	Enables response to BAR memory accesses This field can be freely written during runtime..
0	0x0	RESERVED	RO	constant=0b0

Mnemonic	AFU_MAC.CFG.ICE1SYID
Name	OpenCAPI Function 1 MMIO Subsystem ID & Subsystem Vendor ID Register
Reset Value	0
Description	Function 1 Subsystem ID and Subsystem Vendor ID
VHDL	Value
Name	0b00000, 0b00, 0b000, 0b00, 0b0, 0b00, 0b0000, 0b0, 0b0000000, 0b0, 0b0, 0b0, 0b00
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0001002c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:0	0	RESERVED	RO	constant=0b00000110001101100001000000010100

Mnemonic	AFU_MAC.CFG.ICEAFUEN
Name	OpenCAPI AFU Control DVSEC AFU Enable and ID Register
Reset Value	0
Description	This register contains AFU controls and PASID processing data.
VHDL	Value
Name	AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(31), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(30), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(29), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(28), 0b00, AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(25), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(24), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(23), 0b00, AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(20), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(19), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(18), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(17), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(16), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(15), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(14), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(13), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(12), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(11), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(10), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(9), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(8), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(7), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(6), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(5), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(4), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(3), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(2), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_00C_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0001050c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:28	0	ICEAFUEN_AFU_UNIQUE	RW	These bits are defined by each specific AFU implementation This field can be freely written during runtime.
27:26	0	RESERVED	RO	constant=0b00
25	0	ICEAFUEN_FENCE_AFU	RW	Not supported in OCMB. This field is not disruptive to write during runtime.
24	0	ICEAFUEN_ENABLE_AFU	RW	Allows the AFU to send Commands and Data on the OpenCAPI link. Does not affect receiving commands or sending responses. This field is disruptive to write during runtime.
23	0	ICEAFUEN_RESET_AFU	WO	Not supported in OCMB. WO from OC config space. This field can be freely written during runtime.
22:21	0	RESERVED	RO	constant=0b00
20	0	ICEAFUEN_TERMINATE_VALID	RWX	PASID Termination Valid. Not supported in OCMB. This bit will stay on for 15 CFG clock cycles (375 us @ 400MHz) before resetting. RWX from OC config space. This field can be freely written during runtime.
19:0	0	ICEAFUEN_PASID_TERMINATION_VALUE	RW	PASID to terminate. Not supported in OCMB.

Mnemonic	AFU_MAC.CFG.ICEATAGB
Name	OpenCAPI AFU Control DVSEC acTAG Register
Reset Value	0
Description	This register contains acTag support information
VHDL	Value
Name	0b00000000000000000000, AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(11), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(10), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(9), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(8), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(7), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(6), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(5), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(4), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(3), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(2), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_01C_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0001051c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:12	0	RESERVED	RO	constant=0b00000000000000000000
11:0	0	ICEATAGB_AFU_ACTAG_BASE	RW	This is the first acTag this AFU is allowed to use. This field is disruptive to write during runtime.

Mnemonic	AFU_MAC.CFG.ICEATAGL
Name	OpenCAPI AFU Control DVSEC acTAG Length Register
Reset Value	0
Description	This register contains AFU acTag Length information
VHDL	Value
Name	0b0000, AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(27), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(26), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(25), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(24), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(23), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(22), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(21), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(20), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(19), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(18), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(17), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_018_q(16), 0b000000000000000, 0b0
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00010518
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:28	0	RESERVED	RO	constant=0b0000
27:16	0	ICEATAGL_AFU_ACTAG_LENGTH_ENABLED	RW	Number of consecutive acTags this AFU is allowed to use This field is disruptive to write during runtime.
15:0	0	RESERVED	RO	constant=0b0000000000000001

Mnemonic	AFU_MAC.CFG.ICEFTAG
Name	OpenCAPI Function acTAG Register
Reset Value	0
Description	This register is set up by the host and indicates the base acTAG and number of acTAGs that can be used.
VHDL	Value
Name	0b0000, AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(27), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(26), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(25), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(24), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(23), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(22), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(21), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(20), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(19), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(18), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(17), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(16), 0b0000, AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(11), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(10), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(9), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(8), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(7), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(6), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(5), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(4), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(3), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(2), AFU_MAC.CFG.CFG.CFG_F1.reg_ofunc_00C_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0001030c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:28	0	RESERVED	RO	constant=0b0000
27:16	0	ICEFTAG_ACTAG_BASE	RW	Starting acTag that can be used by this Function. This field is disruptive to write during runtime.
15:12	0	RESERVED	RO	constant=0b0000
11:0	0	ICEFTAG_ACTAG_LENGTH	RW	Number of consecutive acTags this Function is allowed to use. This field is disruptive to write during runtime.

Mnemonic	AFU_MAC.CFG.ICEPIDB
Name	OpenCAPI AFU Control DVSEC PASID Base Register
Reset Value	0
Description	This register contains AFU metadata and PASID controls
VHDL	Value
Name	0b0, AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(30), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(29), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(28), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(27), 0b0000000, AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(19), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(18), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(17), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(16), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(15), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(14), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(13), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(12), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(11), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(10), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(9), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(8), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(7), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(6), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(5), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(4), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(3), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(2), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_014_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00010514
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31	0	RESERVED	RO	constant=0b1
30	0	ICEPIDB_METADATA_ENABLED	RW	Metadata enabled. RW from OC config space This field is disruptive to write during runtime. Dial enums: METADATA_IS_NOT_ENABLED=>0b0 METADATA_IS_ENABLED=>0b1
29:27	0	ICEPIDB_HTRL	RW	Not used in OpenCAPI v3.x. Has no effect in OCMB. Reserved for use in OpenCAPI v4.0 devices. This field can be freely written during runtime.
26:20	0	RESERVED	RO	constant=0b0000000
19:0	0	ICEPIDB_PASID_BASE	RW	First PASID this AFU is allowed to use. RW from OC config space This field is disruptive to write during runtime.

Mnemonic	AFU_MAC.CFG.ICEPIDL
Name	OpenCAPI AFU Control DVSEC PASID Length Register
Reset Value	0
Description	This register contains AFU PASID controls
VHDL	Value
Name	0b0000000000000000000, AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_010_q(12), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_010_q(11), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_010_q(10), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_010_q(9), AFU_MAC.CFG.CFG.CFG_F1.reg_octrl00_010_q(8), 0b00000000
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00010510
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:13	0	RESERVED	RO	constant=0b0000000000000000000
12:8	0	ICEPIDL_PASID_LENGTH_ENABLED	RW	Number of consecutive PASIDs this AFU is allowed to use = 2^pasid_length_enabled RW from OC config space Valid PASID range = pasid_base + ((2^pasid_length_enabled)-1) This field is disruptive to write during runtime.
7:0	0	RESERVED	RO	constant=0b00000000

Mnemonic	AFU_MAC.CFG.ICERCAP
Name	OpenCAPI TLX Receive Template 31-0 Capabilities Register
Reset Value	0
Description	Indicates which receive templates OCMB supports. Gemini supports receive templates 4, 1 & 0
VHDL	Value
Name	AFU_MAC.CFG.CFG.rcv_tmpl_cap_7_q, AFU_MAC.CFG.CFG.rcv_tmpl_cap_4_q, AFU_MAC.CFG.CFG.rcv_tmpl_cap_1_q, AFU_MAC.CFG.CFG.rcv_tmpl_cap_0_q [X]
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0000021c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:8	0	RESERVED	RO	constant=0b000000000000000000000000
7	0	ICERCAP_TEMPLATE_7	RO	When set indicates that Template 7 is supported. This field is disruptive to write during runtime.
6:5	0	RESERVED	RO	constant=0b00
4	0	ICERCAP_TEMPLATE_4	RO	When set indicates that Template 4 is supported. This field is disruptive to write during runtime.
3:2	0	RESERVED	RO	constant=0b00
1	0	ICERCAP_TEMPLATE_1	RO	When set indicates that Template 1 is supported. This field is disruptive to write during runtime.
0	0	ICERCAP_TEMPLATE_0	RO	When set indicates that Template 0 is supported. This field is disruptive to write during runtime.

Mnemonic	AFU_MAC.CFG.ICERRATE
Name	OpenCAPI TLX Flit Receive Rate per Template 7-0 Capabilities Register
Reset Value	0
Description	Indicates the receive rate that can be supported for templates 7-0 by Gemini
VHDL	Value
Name	AFU_MAC.CFG.CFG.rcv_rate_cap_7_q(3), AFU_MAC.CFG.CFG.rcv_rate_cap_7_q(2), AFU_MAC.CFG.CFG.rcv_rate_cap_7_q(1), AFU_MAC.CFG.CFG.rcv_rate_cap_7_q(0), 0b00000000, AFU_MAC.CFG.CFG.rcv_rate_cap_4_q(3), AFU_MAC.CFG.CFG.rcv_rate_cap_4_q(2), AFU_MAC.CFG.CFG.rcv_rate_cap_4_q(1), AFU_MAC.CFG.CFG.rcv_rate_cap_4_q(0), 0b00000000, AFU_MAC.CFG.CFG.rcv_rate_cap_1_q(3), AFU_MAC.CFG.CFG.rcv_rate_cap_1_q(2), AFU_MAC.CFG.CFG.rcv_rate_cap_1_q(1), AFU_MAC.CFG.CFG.rcv_rate_cap_1_q(0), AFU_MAC.CFG.CFG.rcv_rate_cap_0_q(3), AFU_MAC.CFG.CFG.rcv_rate_cap_0_q(2), AFU_MAC.CFG.CFG.rcv_rate_cap_0_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0000024c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:28	0	ICERRATE_TEMPLATE_7	RO	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 7. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
27:20	0	RESERVED	RO	constant=0b00000000
19:16	0	ICERRATE_TEMPLATE_4	RO	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 4. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
15:8	0	RESERVED	RO	constant=0b00000000
7:4	0	ICERRATE_TEMPLATE_1	RO	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 1. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
3:0	0	ICERRATE_TEMPLATE_0	RO	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 0. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.

Mnemonic	AFU_MAC.CFG.ICETCFG
Name	OpenCAPI TLX Transmit Template Configurations Register
Reset Value	0x00000001
Description	The host must set this to indicate which Transmit Templates Gemini should use. Note that Templates 0, 1 & 5 are supported by Gemini. Template 0 must always be supported.
VHDL	Value
Name	AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(31), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(30), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(29), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(28), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(27), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(26), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(25), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(24), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(23), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(22), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(21), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(20), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(19), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(18), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(17), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(16), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(15), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(14), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(13), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(12), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(11), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(10), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(9), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(8), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(7), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(6), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(5), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(4), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(3), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(2), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_024_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00000224
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31	0x0	ICETCFG_TEMPLATE_31	RW	When set indicates that Template 31 is supported. This field is disruptive to write during runtime.
30	0x0	ICETCFG_TEMPLATE_30	RW	When set indicates that Template 30 is supported. This field is disruptive to write during runtime.
29	0x0	ICETCFG_TEMPLATE_29	RW	When set indicates that Template 29 is supported. This field is disruptive to write during runtime.
28	0x0	ICETCFG_TEMPLATE_28	RW	When set indicates that Template 28 is supported. This field is disruptive to write during runtime.
27	0x0	ICETCFG_TEMPLATE_27	RW	When set indicates that Template 27 is supported. This field is disruptive to write during runtime.
26	0x0	ICETCFG_TEMPLATE_26	RW	When set indicates that Template 26 is supported. This field is disruptive to write during runtime.
25	0x0	ICETCFG_TEMPLATE_25	RW	When set indicates that Template 25 is supported. This field is disruptive to write during runtime.
24	0x0	ICETCFG_TEMPLATE_24	RW	When set indicates that Template 24 is supported. This field is disruptive to write during runtime.
23	0x0	ICETCFG_TEMPLATE_23	RW	When set indicates that Template 23 is supported. This field is disruptive to write during runtime.
22	0x0	ICETCFG_TEMPLATE_22	RW	When set indicates that Template 22 is supported. This field is disruptive to write during runtime.
21	0x0	ICETCFG_TEMPLATE_21	RW	When set indicates that Template 21 is supported. This field is disruptive to write during runtime.
20	0x0	ICETCFG_TEMPLATE_20	RW	When set indicates that Template 20 is supported. This field is disruptive to write during runtime.
19	0x0	ICETCFG_TEMPLATE_19	RW	When set indicates that Template 19 is supported. This field is disruptive to write during runtime.
18	0x0	ICETCFG_TEMPLATE_18	RW	When set indicates that Template 18 is supported. This field is disruptive to write during runtime.
17	0x0	ICETCFG_TEMPLATE_17	RW	When set indicates that Template 17 is supported. This field is disruptive to write during runtime.
16	0x0	ICETCFG_TEMPLATE_16	RW	When set indicates that Template 16 is supported. This field is disruptive to write during runtime.
15	0x0	ICETCFG_TEMPLATE_15	RW	When set indicates that Template 15 is supported. This field is disruptive to write during runtime.
14	0x0	ICETCFG_TEMPLATE_14	RW	When set indicates that Template 14 is supported. This field is disruptive to write during runtime.
13	0x0	ICETCFG_TEMPLATE_13	RW	When set indicates that Template 13 is supported. This field is disruptive to write during runtime.
12	0x0	ICETCFG_TEMPLATE_12	RW	When set indicates that Template 12 is supported. This field is disruptive to write during runtime.
11	0x0	ICETCFG_TEMPLATE_11	RW	When set indicates that Template 11 is supported. This field is disruptive to write during runtime.
10	0x0	ICETCFG_TEMPLATE_10	RW	When set indicates that Template 10 is supported. This field is disruptive to write during runtime.
9	0x0	ICETCFG_TEMPLATE_9	RW	When set indicates that Template 9 is supported. This field is disruptive to write during runtime.
8	0x0	ICETCFG_TEMPLATE_8	RW	When set indicates that Template 8 is supported. This field is disruptive to write during runtime.
7	0x0	ICETCFG_TEMPLATE_7	RW	When set indicates that Template 7 is supported. This field is disruptive to write during runtime.
6	0x0	ICETCFG_TEMPLATE_6	RW	When set indicates that Template 6 is supported. This field is disruptive to write during runtime.
5	0x0	ICETCFG_TEMPLATE_5	RW	When set indicates that Template 5 is supported. This field is disruptive to write during runtime.
4	0x0	ICETCFG_TEMPLATE_4	RW	When set indicates that Template 4 is supported. This field is disruptive to write during runtime.
3	0x0	ICETCFG_TEMPLATE_3	RW	When set indicates that Template 3 is supported. This field is disruptive to write during runtime.
2	0x0	ICETCFG_TEMPLATE_2	RW	When set indicates that Template 2 is supported. This field is disruptive to write during runtime.
1	0x0	ICETCFG_TEMPLATE_1	RW	When set indicates that Template 1 is supported. This field is disruptive to write during runtime.
0	0x1	ICETCFG_TEMPLATE_0	RW	When set indicates that Template 0 is supported. This field is disruptive to write during runtime.

Mnemonic	AFU_MAC.CFG.ICETRATE
Name	OpenCAPI TLX Flit Transmit Rate per Templates 7-0 Configurations Register
Reset Value	0
Description	Indicates the transmit rate that can be supported for templates 7-0 for Gemini
VHDL	Value
Name	AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(31), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(30), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(29), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(28), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(27), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(26), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(25), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(24), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(23), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(22), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(21), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(20), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(19), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(18), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(17), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(16), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(15), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(14), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(13), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(12), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(11), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(10), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(9), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(8), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(7), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(6), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(5), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(4), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(3), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(2), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_06C_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x0000026c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:28	0	ICETRATE_TEMPLATE_7	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 7. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
27:24	0	ICETRATE_TEMPLATE_6	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 6. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
23:20	0	ICETRATE_TEMPLATE_5	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 5. A value of zero indicates that a control flit can be sent in the following flit cycle. This field is disruptive to write during runtime.
19:16	0	ICETRATE_TEMPLATE_4	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 4. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
15:12	0	ICETRATE_TEMPLATE_3	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 3. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
11:8	0	ICETRATE_TEMPLATE_2	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 2. A value of zero indicates that a control flit can be sent in the following flit cycle. This field can be freely written during runtime.
7:4	0	ICETRATE_TEMPLATE_1	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 1. A value of zero indicates that a control flit can be sent in the following flit cycle. This field is disruptive to write during runtime.
3:0	0	ICETRATE_TEMPLATE_0	RW	Indicates the size of gap (measured in flits) before the next control flit can be sent for Template 0. A value of zero indicates that a control flit can be sent in the following flit cycle. This field is disruptive to write during runtime.

Mnemonic	AFU_MAC.CFG.ICEVER
Name	OpenCAPI Transport Layer Configuration Register
Reset Value	0x31000000
Description	This register is configured by the host to indicate the level of OpenCAPI TL specification OCMB must use.
VHDL	Value
Name	AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(31), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(30), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(29), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(28), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(27), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(26), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(25), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(24), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(23), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(22), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(21), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(20), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(19), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(18), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(17), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(16), 0b00000000, AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(7), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(6), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(5), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(4), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(3), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(2), AFU_MAC.CFG.CFG.CFG_F0.reg_otl0_010_q(1:0)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
CFG	0x00000210
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
31:24	0x31	ICEVER_TL_MAJOR_VERSION_CONFIGURATION	RW	Indicates, x, the major version of OpenCAPI TL specification OCMB must use (as in version x.y. For example v3.1) This field can be freely written during runtime.
23:16	0x0	ICEVER_TL_MINOR_VERSION_CONFIGURATION	RW	Indicates, y, the minor version of OpenCAPI TL specification OCMB must use (as in version x.y. For example v3.1) This field is disruptive to write during runtime.
15:8	0x0	RESERVED	RO	constant=0b00000000
7:4	0x0	ICEVER_LONG_BACK_OFF_TIMER	RW	Long back off timer for long back-off retry responses. Not supported in OCMB. This field can be freely written during runtime.
3:0	0x0	ICEVER_SHORT_BACK_OFF_TIMER	RW	Short back off timer for short back-off retry responses. This field is disruptive to write during runtime.

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICECFG0
Name	ICE Configuration Register 0
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.CFG0.CFG_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801240c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICECFG0_TBD	RW	Default register used for operations targeting unimplemented registers.

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICECFG1
Name	ICE Configuration Register 1
Reset Value	0x0000040000450000
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.CFG1.CFG_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801240d
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0	0x0	ICECFG1_TRAP_CLEAR	RW	when set, all trap and hold registers will be cleared
1	0x0	ICECFG1_INJECT_XSTOP	RW	When set will inject a channel checkstop error to be reported to the host via the interrupt interface Interrupts are generated on the rising edge of an error. To inject a second interrupt of this type the bit will need to be cleared and then set again.
2	0x0	ICECFG1_INJECT_MCHK	RW	When set will inject aapplication interrupt to be reported to the host via the interrupt interface Interrupts are generated on the rising edge of an error. To inject a second interrupt of this type the bit will need to be cleared and then set again.
3	0x0	ICECFG1_TRAP_UPDATE	RW	when set, trap updates every cycle and does not freeze on error
4	0x0	ICECFG1_HOLD_ACUM	RW	when set, hold reg acumulates on error and does not freeze on fir error out
5	0x0	ICECFG1_FORCE_RECAL	RW	Force xilinx memory controller recalibration.
6	0x0	ICECFG1_AUTO_RECAL_DISABLE	RW	Disable automatic recalibration of xilinx memory controller on calibration fail.
7	0x0	ICECFG1_MEM_INIT_START	RW	Start Memory initialization sequence
8	0x0	ICECFG1_MEM_INIT_ZERO	RW	when set, Initialize memory to all 0 data, otherwise initialize with address as data.
9:15	0x0	ICECFG1_TBD	RW	TBD
16:20	0x0	ICECFG1_EDPL_RESERVED0	RW	EDPL Reserved
21	0x1	ICECFG1_EDPL_ENABLE	RW	EDPL Enable
22	0x0	ICECFG1_EDPL_MAX_COUNTER_RESET	RW	EDPL Max Counter Reset
23:31	0x0	ICECFG1_EDPL_RESERVED1	RW	EDPL reserved
32:39	0x0	ICECFG1_EDPL_INJECT_PER_LANE	RW	EDPL Inject Per lane
40	0x0	ICECFG1_EDPL_RESERVED2	RW	EDPL reserved
41:43	0x4	ICECFG1_EDPL_ERROR_THRESHOLD	RW	EDPL Error Threshold
44:47	0x5	ICECFG1_EDPL_TIME_WINDOW	RW	EDPL Time Window
48:51	0x0	ICECFG1_INTRP_CMDFLAG_0	RW	ICE Interrupt handle 0 command flag. Fills the cmd_flag portion of the intrp_re_q command found in section 2.3 of the OpenCAPI TL 3.1 Specification. Used for Channel Checkstop Interrupt Request.
52:55	0x0	ICECFG1_INTRP_CMDFLAG_1	RW	ICE Interrupt handle 1 command flag Fills the 4-bit cmd_flag portion of the intrp_req command found in section 2.3 of the OpenCAPI TL 3.1 Specification. Used for Recoverable Attention Interrupt Request.
56:59	0x0	ICECFG1_INTRP_CMDFLAG_2	RW	ICE Interrupt handle 2 command flag Fills the cmd_flag portion of the intrp_req command found in section 2.3 of the OpenCAPI TL 3.1 Specification. Used for Special Attention Interrupt Request.
60:63	0x0	ICECFG1_INTRP_CMDFLAG_3	RW	ICE Interrupt handle 3 command flag Fills the cmd_flag portion of the intrp_req command found in section 2.3 of the OpenCAPI TL 3.1 Specification. Used for Application Interrupt Request.

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICECFG2
Name	ICE Configuration Register 2
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.CFG2.CFG_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801240e
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:31	0	ICECFG2_ECID	RO	Git hash corresponding to the latest commit used for this version of Gemini
32:63	0	ICECFG2_DEVICE_ID_REG	RO	Device Id information for Gemini 32:35 = Major Release 36:39 = Minor Release 44:47 = Location Code 56:63 = Chip ID

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICEINTHLD0
Name	ICE Interrupt Handle Register 0
Reset Value	0x0000000000000001
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.INTHLD0.CFG_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012410
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0x0000000000000001	ICEINTHLD0_TLXT_INTHLD_0_REG	RW	This field is disruptive to write during runtime. ICE Interrupt Handle Register 0 Used for Channel Checkstop Interrupt Fills the obj_handle portion of the intrp_re_q command found in section 2.3 of the OpenCAPI TL 3.1 Specification.

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICEINTHLD1
Name	ICE Interrupt Handle Register 1
Reset Value	0x0000000000000002
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.INTHLD1.CFG_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012411
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0x0000000000000002	ICEINTHLD1_TLXT_INTHLD_1_REG	RW	This field is disruptive to write during runtime. ICE Interrupt Handle Register 1 Used for Recoverable Attn Interrupt Fills the obj_handle portion of the intrp_req command found in section 2.3 of the OpenCAPI TL 3.1 Specification.

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICEINTHLD2
Name	ICE Interrupt Handle Register 2
Reset Value	0x0000000000000003
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.INTHLD2.CFG_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012412
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0x0000000000000003	ICEINTHLD2_TLXT_INTHLD_2_REG	RW	This field is disruptive to write during runtime. ICE Interrupt Handle Register 2 Used for Special Attn Interrupt Fills the obj_handle portion of the intrp_req command found in section 2.3 of the OpenCAPI TL 3.1 Specification.

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICEINTHLD3
Name	ICE Interrupt Handle Register 3
Reset Value	0x0000000000000004
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.INTHLD3.CFG_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012413
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0x0000000000000004	ICEINTHLD3_TLXT_INTHLD_3_REG	RW	This field is disruptive to write during runtime. ICE Interrupt Handle Register 3 Used for Application Interrupt Fills the obj_handle portion of the intrp_req command found in section 2.3 of the OpenCAPI TL 3.1 Specification.

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP0
Name	ICE Trap Register 0
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP0.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012424
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICETRAP0_DEBUG_BUS	ROX	TLX Parser Trace 0 = dlx_tlx_link_up 1 = dlx_tlx_flit_crc_err 2 = dlx_tlx_flit_valid 3 = data_rx 4:7 = dlx_tlx_flit(451 downto 448) - this is the data runlength 8:13 = dlx_tlx_flit(465 downto 460) - this is the template type 14:17 = cflit(451 downto 448) - runlength in use on output of input fifo 18:23 = cflit(465 downto 460) template in use on output of input fifo 24 = dl_full - the input fifo is full 25 = start_ctl - start to parse a control flit 26:29 = parse_st - counts thru possible slots in the template looking for cmd packets 30:37 = packet_q(7:0) - opcode of parser output 38:40 = packet_q(111 downto 109) - length (pl or dl) of parser packet output 41 = dcp_we - write enable strobe for data (command data or config data) 42:47 = cmdd_w_crc_q - count of cmd data that is in the cmd data fifo and has good crc (units of 64B) 48 = cfg_data_empty - fifo for config write data has nothing with good crc in it 49 = cmd write - write a command packet into the command fifo 50 = cfg_write - write a config command into the config fifo 51 = ds_write - write an entry into the data steering fifo 52:59 = ds_din - data steering fifo entry contains cmd/cfg flag and address offset if cfg. 60 = resp_write - write an intrp_resp packet to the resp fifo 61 = resp_cred_ok - there is enough credit for tlx to send a response to afu 62 = cmd_cred_ok - there is enough credit for tlx to send a command to afu 63 = cfg_cred_ok - there is enough credit for tlx to send a config command to the cfg

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP1
Name	ICE Trap Register 1
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP1.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012425
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICETRAP1_DEBUG_BUS	ROX	AFU Debug 0:40 = TBD 41 = Response data credit available 42 = Response command credit available 43 = Data for DRAM 44 = Data for MMIO 45 = Data size indicator 46 = Data port indicator 47 = MMIO write command data valid 48:49 = Command valid indictor to async fifo 50 = Command size 51 = Port indicator 52 = MMIO command fifo credit available 53 = Port 1 read command async fifo credit available 54 = Port 0 read command async fifo credit available 55 = Port 1 write command async fifo credit available 56 = Port 0 write command async fifo credit available 57:58 = yield_q(1:0); Yield signals to response arbiter 59 = data_ctrl_fifo_dat_out_val; Valid write control command in FIFO 60 = cmd_fifo_dat_out_val; Valid command in command FIFO 61 = cmdmmio_q; MMIO command 62 = cmdval_q; DRAM command is valid 63 = cmdrdy_q; CMD FIFO is ready to accept new commands

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP2
Name	ICE Trap Register 2
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP2.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012426
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICETRAP2_DEBUG_BUS	ROX	MMIO/error Reporting Trace 0 = xlate_mmio_cmd_val 1 = xlate_mmi_cmd_rd 2:17 = xlate_mmio_cmd_tag 18 = cmd_pop_q 19 = cmd_data_out(0) 20:35 = cmd_data_out(51:36) 36:53 = sc_addr_v 54:56 = cmd_addr_offset(2:0) 57:58 = intrp_req_chan_xstop 59:60 = intrp_req_app_intrp

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP3
Name	ICE Trap Register 3
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP3.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012427
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICETRAP3_DEBUG_BUS	ROX	TLX Framer Trace 0 = rsp_valid_d1 1 = injct_cfg_rsp 2:4 = rsp_packet_reg(2:0) 5:20 = rsp_packet_reg(23:8) 21 = valid_rsp_leaving_fifo 22:24 = vc0_fifo_output_reg(2:0) 25:40 = vc0_fifo_output_reg(23:8) 41:43 = rsp_tmpl 44 = rsp_cf_was_taken 45:48 = rcf_df_count_last 49:52 = meta_run_length 53:56 = framer_run_length 57 = metadata_enabled 58:60 = meta_packet_ptr(2:0) 61:63 = meta_packet_ptr(2:0)

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP4
Name	ICE
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP4.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012428
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICETRAP4_DEBUG_BUS	ROX	0 = Port_0_PHY_Cal_finished 1 = Port_1_PHY_Cal_finished 2:63 = TBD 24:31 = Calibration Retry Counter 32 = Memory Initialization Complete 33 = Memory Initialization in Progress 34 = Memory Initialization is waiting for MC user Interface write credits 35:63 = Memory Initialization current 64B write address

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP5
Name	ICE
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP5.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012429
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:31	0	ICETRAP5_DLX_DEBUG_REG04	ROX	DLX Debug Reg 04
32:63	0	ICETRAP5_DLX_DEBUG_REG05	ROX	DLX debug Reg 05

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP6
Name	ICE
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP6.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801242a
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:31	0	ICETRAP6_DLX_DEBUG_REG06	ROX	DLX Debug Reg06
32:63	0	ICETRAP6_DLX_DEBUG_REG07	ROX	DLX Debug Reg07

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP7
Name	ICE
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP7.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801242b
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICETRAP7_UI_ERR_DEBUG_BUS	ROX	0:4 = TBD 5 = Port1 WD Fifo, Host Side 6 = Port1 WD Fifo MCtrl Side 7 = Port1 CM Fifo, Host Side 8 = Port1 CM Fifo MCtrl Side 9 = Port1 RD Fifo, MCtrl Side 10 = Port1 RD Fifo Host Side 11 = Port1 RS Fifo, MCtrl Side 12 = Port1 RS Fifo Host Side 13 = Port1 WS Fifo, MCtrl Side 14 = Port1 WS Fifo Host Side 15 = Port0 WD Fifo, Host Side 16 = Port0 WD Fifo MCtrl Side 17 = Port0 CM Fifo, Host Side 18 = Port0 CM Fifo MCtrl Side 19 = Port0 RD Fifo, MCtrl Side 20 = Port0 RD Fifo Host Side 21 = Port0 RS Fifo, MCtrl Side 22 = Port0 RS Fifo Host Side 23 = Port0 WS Fifo, MCtrl Side 24 = Port0 WS Fifo Host Side 25 = Parity error Port1 26:33 = Calculated Parity error on Read response (PIN) 34:41 = Calculated Parity error on Read Response (CHIP) 42:49 = Calculated Parity error on Read Response (LINE)

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICETRAP8
Name	ICE
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.TRAP8.TRAP_REG_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801242c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICETRAP8_DEBUG_BUS	ROX	TBD

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICE_ERR0_REPORTQ
Name	ICE Error report register 0
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.ERR0.ERR_ACUM_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801241c
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0	0	ICE_ERR0_REPORTQ_DLX_VALID_AND_ERR_SAME_CYC	ROX	DLX Supplying TLX Receive a valid and error on the same cycle
1	0	ICE_ERR0_REPORTQ_DATA_RUN_LENGTH_ERR	ROX	TLX Received data run length greater than 8
2	0	ICE_ERR0_REPORTQ_INPUT_FIFO_OVERFLOW	ROX	TLX Receive Input FIFO overflowed
3	0	ICE_ERR0_REPORTQ_INPUT_FIFO_UNDERFLOW	ROX	TLX Receive input fifo underflowed
4	0	ICE_ERR0_REPORTQ_UNEXPECTED_COLL	ROX	MMIO response and DRAM response request received same cycle
5	0	ICE_ERR0_REPORTQ_CMD_DATA_COUNT_UNDERFLOW	ROX	TLX_RCV Cmd good data count underflow
6	0	ICE_ERR0_REPORTQ_CMD_DATA_COUNT_OVERFLOW	ROX	TLX_RCV Cmd good data count overflow
7	0	ICE_ERR0_REPORTQ_DAT_STEER_FIFO_UNDERFLOW	ROX	TLX_RCV Data Steering fifo underflowed
8	0	ICE_ERR0_REPORTQ_DAT_STEER_FIFO_OVERFLOW	ROX	TLX_RCV Data Steering fifo overflowed
9	0	ICE_ERR0_REPORTQ_RSP_FIFO_UNDERFLOW	ROX	TLX_RCV response fifo underflowed
10	0	ICE_ERR0_REPORTQ_RSP_FIFO_OVERFLOW	ROX	TLX_RCV response fifo overflowed
11	0	ICE_ERR0_REPORTQ_CMD_DATA_FIFO_UNDERFLOW	ROX	TLX_RCV Command fifo underflowed
12	0	ICE_ERR0_REPORTQ_CMD_DATA_FIFO_OVERFLOW	ROX	TLX_RCV Command fifo Overflowed
13	0	ICE_ERR0_REPORTQ_INVLID_VALUE_ON_RD_CNT	ROX	Invalid value supplied on afu_tlx_cmd_rd_cnt
14	0	ICE_ERR0_REPORTQ_ARRAY_OVERFLOW_IN_INPUT_FIFO	ROX	Array overflow in input fifo
15	0	ICE_ERR0_REPORTQ_RCV_CMD_FIFO_UNDERFLOW	ROX	TLX_RCV Command fifo underflowed
16	0	ICE_ERR0_REPORTQ_RCV_CMD_FIFO_OVERFLOW	ROX	TLX_RCV Command Fifo Overflowed
17	0	ICE_ERR0_REPORTQ_CFG_FIFO_UNDERFLOW	ROX	Config Fifo Underflowed
18	0	ICE_ERR0_REPORTQ_CFG_FIFO_OVERFLOW	ROX	Config Fifo Overflowed
19	0	ICE_ERR0_REPORTQ_CFG_DATA_OVERFLOW	ROX	Config Data Overflow
20	0	ICE_ERR0_REPORTQ_CFG_DATA_UNDERFLOW	ROX	Config Data Underflow
21	0	ICE_ERR0_REPORTQ_BAD_TEMPLATE	ROX	Bad Template. Template was not 0x0, 0x1, or 0x4
22	0	ICE_ERR0_REPORTQ_BAD_MMIO_LENGTH	ROX	Bad length for MMIO read or write (length must be 8 Bytes
23	0	ICE_ERR0_REPORTQ_UNKNOWN_OPCODE	ROX	Unknown Opcode received in TLX from Host
24	0	ICE_ERR0_REPORTQ_BAD_OP_LENGTH	ROX	Invalid length for DRAM operation received in TLX from HOST
25	0	ICE_ERR0_REPORTQ_CRED_RTN_ILLEGAL_SLOT	ROX	Return_tlx_credits not in slots 0/1
26:30	0	ICE_ERR0_REPORTQ_TBD_PARSER	ROX	TBD_Parser
31	0	ICE_ERR0_REPORTQ_MEMCTL_FLAG_ONE	ROX	INFO: mem_cntl with a flag of 0001 received
32	0	ICE_ERR0_REPORTQ_AFU_CMD_FIFO_OVERFLOW	ROX	Afu Command Fifo Overflow
33	0	ICE_ERR0_REPORTQ_AFU_CMD_FIFO_UNDERFLOW	ROX	AFU Command FIFO underflow
34	0	ICE_ERR0_REPORTQ_WR_DAT_CNTL_FIFO_OVERFLOW	ROX	AFU Write Data Control Fifo Overflow
35	0	ICE_ERR0_REPORTQ_WR_DAT_CNTL_FIFO_UNDERFLOW	ROX	AFU Write Data Control FIFO underflow
36	0	ICE_ERR0_REPORTQ_RESP_COLLISION	ROX	MMIO response and DRAM response request received same cycle
37	0	ICE_ERR0_REPORTQ_RESP_CRD_OVER_INITIAL	ROX	Response Credit counters exceeded Initial Credit
38	0	ICE_ERR0_REPORTQ_UNEXPECTED_WR_DATA	ROX	AFU received unexpected write data
39	0	ICE_ERR0_REPORTQ_CMD_CNTL_PERR	ROX	CMD control parity error
40	0	ICE_ERR0_REPORTQ_MAX_ASYNC_FIFO_CRD_EXCEEDED	ROX	Max Asynchronous FIFO credit exceeded
41	0	ICE_ERR0_REPORTQ_AFU_RECEIVED_UNSUPPORTED_CMD	ROX	AFU received unsupported commands from TLX
42	0	ICE_ERR0_REPORTQ_RESP_CRD_COUNTER_UNDERFLOW	ROX	Response credit counter underflow
43	0	ICE_ERR0_REPORTQ_UNSUPP_DATA_LENGTH	ROX	AFU received command with unsupported Data Length
44	0	ICE_ERR0_REPORTQ_UI_ERR	ROX	UI Error
45:46	0	ICE_ERR0_REPORTQ_AFU_TBD	ROX	AFU TBD
47	0	ICE_ERR0_REPORTQ_INJECT_XSTOP	ROX	Checkstop Injected via Config 1 Register
48	0	ICE_ERR0_REPORTQ_TLX_CRD_OVERFLOW	ROX	TLX Credit Overflow
49	0	ICE_ERR0_REPORTQ_HARDWARE_SHIFT_ERROR	ROX	Hardware Shift Error
50	0	ICE_ERR0_REPORTQ_META_FIFO_OVERFLOW	ROX	meta_fifo_overflow
51	0	ICE_ERR0_REPORTQ_META_FIFO_UNDERFLOW	ROX	Metadata Fifo Overflow
52	0	ICE_ERR0_REPORTQ_DCP0_DATA_FIFO_OVERFLOW	ROX	DCP0 Data Fifo Overflow
53	0	ICE_ERR0_REPORTQ_DCP0_DATA_FIFO_UNDERFLOW	ROX	dcp0_data_fifo_underflow
54	0	ICE_ERR0_REPORTQ_VC3_CMD_FIFO_OVERFLOW	ROX	vc3_cmd_fifo_overflow
55	0	ICE_ERR0_REPORTQ_VC3_CMD_FIFO_UNDERFLOW	ROX	VC3 cmd Fifo Underflow
56	0	ICE_ERR0_REPORTQ_VC0_RESP_FIFO_OVERFLOW	ROX	VC0 resp Fifo Overflow
57	0	ICE_ERR0_REPORTQ_VC0_RESP_FIFO_UNDERFLOW	ROX	vc0_resp_fifo_underflow
58	0	ICE_ERR0_REPORTQ_META_PKT_PTR_OVER_MAX	ROX	Meta Packet Ptr Over Max
59	0	ICE_ERR0_REPORTQ_ROGUE_RESP_DATA	ROX	Rogue response data
60	0	ICE_ERR0_REPORTQ_METADATA_ERR	ROX	Read attempted with metadata enabled but no template which supports metadata
61	0	ICE_ERR0_REPORTQ_RESP_DATA_MISSING	ROX	Response Data Missing
62	0	ICE_ERR0_REPORTQ_CTRL_REG_PERR	ROX	Control Register Parity Error
63	0	ICE_ERR0_REPORTQ_INFO_REG_PERR	ROX	Informational Register Parity Error

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICE_ERR0_REPORTQ_MASK
Name	ICE ERROR Report Mask Register 0
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.ERR0.ERR_MASK_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012414
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICE_ERR0_REPORTQ_MASK_ERRMASK	RW	This field is disruptive to write during runtime. Mask for ICE Error Report 0 bits 0:63

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICE_ERR1_REPORTQ
Name	ICE Error report register
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.ERR1.ERR_ACUM_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801241d
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICE_ERR1_REPORTQ_TBD	ROX	TBD

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICE_ERR1_REPORTQ_MASK
Name	ICE ERROR Report Mask Register 1
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.ERR1.ERR_MASK_Q(0:63)
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012415
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:63	0	ICE_ERR1_REPORTQ_MASK_ERRMASK	RW	This field is disruptive to write during runtime. Mask for ICE Error Report 1 bits 0:63

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICE_ERR2_REPORTQ
Name	ICE Error report register
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.ERR2.ERR_ACUM_Q(0:31), 0b00000000000000000000000000000000
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x0801241e
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:31	0	ICE_ERR2_REPORTQ_TBD	ROX	TBD
32:63	0	RESERVED	RO	constant=0b00000000000000000000000000000000

Mnemonic	AFU_MAC.MMIO.ICE_REGS.ICE_ERR2_REPORTQ_MASK
Name	ICE ERROR Report Mask Register 1
Reset Value	0
Description
VHDL	Value
Name	AFU_MAC.MMIO.ICE_REGS.ERR2.ERR_MASK_Q(0:31), 0b00000000000000000000000000000000
ParityName	NONE
ParityErrorName	NONE
WriteEnableName	NONE
AddrType	Address
SCOM	0x08012416
AttributeType	AttributeValue

Bit Range	InitialValue	FieldName	FieldType	Description
0:31	0	ICE_ERR2_REPORTQ_MASK_ERRMASK	RW	This field is disruptive to write during runtime. Mask for ICE Error Report 2 bits 0:31
32:63	0	RESERVED	RO	constant=0b00000000000000000000000000000000

## ICE Configuration Sequence
Note: Bit notation used is 31:0 with 0 being the lsb and all OpenCAPI configuration registers are 32-bit and little endian.

Config Read Device and Vendor ID
ICE0ID - Config read addr x00000000 = x06361014
Other identifiers that may be optionally read for sanity check:
ICE0SYID – Config read addr x0000002C
ICE1DID – Config read addr x00010000 = x06361014
ICE1SYID – Config read addr x0001002C

Config write to establish which transmit templates and rates are used
ICETCFG – Config write addr x00000224; specifically bits 5, 1 & 0 for supported Transmit templates x5, x1 & x0 respectively
ICETRATE – Config write addr x00000268; specifically bits 23:20, bits 7:4 & bits 3:0 for supported Transmit templates x5, x1, x0 respectively. These values may depend on link speed.

Config write to set short back off timer & OpenCAPI TL Minor Version
ICEVER – Config write addr x00000210; specifically bits 23:16 for the TL Minor Version and bits 3:0 for the Short back off timer

Config Read to establish which receive templates and receive template rates are supported. Note ICE only supports receive templates 4, 1 & 0.
ICERCAP – Config read addr x0000021C
ICERRATE – Config read addr x0000024C

Config Write to set MMIO BAR0, to identify MMIO space vs. bulk memory
ICE1BARH – Config write addr x00010014

Config Write to Enable Memory space to use BAR0 to distinguish MMIO operations from bulk memory
ICE1MBIT – Config write addr x00010004; specifically bit 1

Config read to determine interrupt capabilities
ICEATAGL – Config read addr x00010518; specifically bits 11:0 for the number of consecutive acTags supported
ICEPIDL – Config read addr x00010510; specifically bits 4:0 for the PASID length supported

Config write to set up interrupt fields
ICEATAGB – Config write x0001051C; specifically bits 11:0 for the AFU acTag base
ICEATAGL – Config write x00010518; specifically bits 27:16 for the AFU acTag enabled length
ICEFTAG – Config write x0001030C; specifically bits 27:16 for the function acTag base and bits 11:0 for the function acTag length
ICEPIDB – Config write addr x00010514; specifically bits 19:0 for the PASID base
ICEPIDL – Config write addr x00010510; specifically bits 4:0 for the PASID enabled length

Config write to enable metadata
ICEPIDB – Config write x00010514; specifically bit 30

Config write to enable AFU
ICEAFUEN – Config write x0001050C; specifically bit 24

## Debug & Error
### TLX Downstream Debug & Error
#### Errors
Signal Name	Description
TLX_MMIO_RCV_ERRORS(31 downto 0)
31	DLX supplying valid and error in the same cycle
30	Data flit runlength more than 8
29	Input fifo overflowed
28	Input fifo underflowed
27	Unexpected collision between start_ctl and write data
26	Cmd good data count underflow
25	Cmd good data count overflow
24	Data steering fifo underflowed
23	Data steering fifo overflowed
22	Response fifo underflowed
21	Response fifo overflowed
20	Command data fifo underflowed
19	Command data fifo overflowed
18	Invalid value supplied on afu_tlx_cmd_rd_cnt
17	Array overflow in input fifo
16	Command fifo underflowed
15	Command fifo overflowed
14	Config fifo underflowed
13	Config fifo overflowed
12	Config data fifo overflowed
11	Config data fifo underflowed
10	Bad template – (not 0 or 1 or 4)
9	Bad length for MMIO read or write (length must be 8 bytes)
8 downto 0	TBD

#### Debug bus
Signal Name		Description
TLX_MMIO_RCV_DEBUG(63 downto 0)
63	0	dlx_tlx_link_up
62	1	dlx_tlx_flit_crc_err
61	2	dlx_tlx_flit_valid
60	3	data_rx
59 downto 56	4:7	dlx_tlx_flit(451 downto 448) – this is the data runlength
55 downto 50	8:13	dlx_tlx_flit(465 downto 460) – this is the template type
49	14	input_overflow
48 downto 47	15:16	reserved
46 downto 41	17:22	cflit(465 downto 460) template in use on output of input fifo
40	23	dl_full – the input fifo is full
39	24	start_ctl – start to parse a control flit
38 downto 35	25:28	parse_st – counts thru possible slots in the template looking for cmd packets
34 downto 27	29:36	packet_q(7:0) – opcode of parser output
26 downto 24	37:39	packet_q(111 downto 109) – length (pl or dl) of parser packet output
23	40	dcp_we – write enable strobe for data (command data or config data)
22 downto 17	41:46	cmdd_w_crc_q – count of cmd data that is in the cmd data fifo and has good crc (units of 64B)
16	47	cfg_data_empty – fifo for config write data has nothing with good crc in it
15	48	cmd write – write a command packet into the command fifo
14	49	cfg_write – write a config command into the config fifo
13	50	ds_write – write an entry into the data steering fifo
12 downto 5	51:58	ds_din – data steering fifo entry contains cmd/cfg flag and address offset if cfg.
4	59	resp_write - write an intrp_resp packet to the resp fifo
3	60	resp_cred_ok - there is enough credit for tlx to send a response to afu
2	61	cmd_cred_ok - there is enough credit for tlx to send a command to afu
1	62	cfg_cred_ok – there is enough credit for tlx to send a config command to the cfg
0	63	tlx_mmio_rcv_errors_q(0)

### AFU Debug & Error

Signal Name	Description
AFU_MMIO_ERR(15 downto 0)
15	Cmd FIFO overflow
14	Cmd FIFO underflow
13	Write data Control FIFO overflow
12	Write data Control FIFO underflow
11	MMIO response and DRAM response request received same cycle
10	Response Credit counters exceeded Initial Credit
9	AFU received unexpected write data
8	CMD control parity error
7	Max Asynchronous FIFO credit exceeded
6	AFU received unsupported commands from TLX
5	Response credit counter underflow
4	AFU received command with unsupported Data Length
3:0	TBD

Signal Name	Description
AFU_MMIO_dbg(63 downto 0)
63:23	TBD
22	Response data credit available
21	Response command credit available
20	Data for DRAM
19	Data for MMIO
18	Data size indicator
17	Data port indicator
16	MMIO write command data valid
15:14	Command valid indictor to async fifo
13	Command size
12	Port indicator
11	MMIO command fifo credit available
10	Port 1 read command async fifo credit available
9	Port 0 read command async fifo credit available
8	Port 1 write command async fifo credit available
7	Port 0 write command async fifo credit available
6:5	yield_q(1:0); Yield signals to response arbiter
4	data_ctrl_fifo_dat_out_val; Valid write control command in FIFO
3	cmd_fifo_dat_out_val; Valid command in command FIFO
2	cmdmmio_q; MMIO command
1	cmdval_q; DRAM command is valid
0	cmdrdy_q; CMD FIFO is ready to accept new commands

Signal Name	Description
UI_MMIO_ERR(49 downto 0)
49:45	TBD
44:35	Port 1 FIFO error / 35: WD Fifo, Host Side / 36: WD Fifo MCtrl Side / 37 : CM Fifo, Host Side / 38 : CM Fifo MCtrl Side / 39 : RD Fifo, MCtrl Side / 40 : RD Fifo Host Side / 41 : RS Fifo, MCtrl Side / 42 : RS Fifo Host Side / 43: WS Fifo, MCtrl Side / 44 : WS Fifo Host Side
34:25	Port 0 FIFO error / 25 : WD Fifo, Host Side / 26: WD Fifo MCtrl Side / 27 : CM Fifo, Host Side / 28 : CM Fifo MCtrl Side / 29 : RD Fifo, MCtrl Side / 30 : RD Fifo Host Side / 31 : RS Fifo, MCtrl Side / 32 : RS Fifo Host Side / 33 : WS Fifo, MCtrl Side / 34 : WS Fifo Host Side
24	Parity Error from Port 1
23:0	indicates a calculated parity error in the respective dimension on the read response / (23:16) : pin / (15:8) : chip / (7:0) : line

Signal Name	Description
UI_MMIO_DBG(1 downto 0)
1	Port 1 Idle indicator
0	Port 0 Idle indicator

Signal Name	Description
MC_MMIO_DBG(63 downto 0)
63	Port 1 PHY calibration is finished
62	Port 0 PHY calibration is finished
61:40	Reserved
39:32	Calibration Retry Counter
31	Memory Initialization Completed
30	Memory Initialization in progress
29	Memory Initialization is waiting for MC user interface write credits
28:0	Memory Initialization current 64B write address